## Slide 1: WF on Uplink DMRS Enhancement for MTC
NEC, ETRI, Huawei, HiSilicon, Intel, Panasonic,
Qualcomm, Sierra Wireless
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th - 29th May 2015
Agenda item 6.2.1.4
R1-153436

## Slide 2: Observations
For Rel-13 MTC coverage enhancement:
  At least in 18 dB coverage enhancement cases, simulation results show that increasing uplink DMRS density could increase SNR by 0.5 - 1 dB and reduce the number of PUSCH repetitions by 3.2 – 30.6%
2
Company | Gain over 1X DMRS in 18 dB coverage enhancement
Nokia Networks (R1-152545) | 0.7 dB (2SF ChEst)
INTERDIGITAL (R1-153250) | 0.5 dB (4SF ChEst)
NTT DOCOMO (R1-153324) | 0.6 dB (4SF ChEst)
Qualcomm Inc. (R1-152765) | 0.8 dB
Intel Corporation (R1-153411) | 1 dB (4SF ChEst)
Panasonic (R1-151665) | 0.8 dB (4SF ChEst)
CATT (R1-152558) | 17.6% (1SF ChEst), 14.1% (4SF ChEst)
NEC (R1-152681) | 23.1% (1SF ChEst), 7.1% (4SF ChEst)
Sierra Wireless (R1-153113) | 3.2 -7.7% (2X DMRS, 3SF ChEst) 7.3-22.0% (4X DMRS, 3SF ChEst)
Samsung (R1-152833) | ~10% (4SF ChEst)
Ericsson (R1-151215) | 30.6% (1SF ChEst), 15.2% (4SF ChEst) for 2X DMRS
ETRI (R1-150517) | 23.2% (1SF ChEst)

## Slide 3: Proposals
Increased uplink DMRS density is supported for PUSCH for UEs operating CE
FFS following solutions
    2X DMRS
    4X DMRS
    Entire DMRS subframe in the beginning of the transmission
    The specification of the new DMRS pattern is on one PRB basis
When to use the new pattern is up to eNB
FFS details of configurability