## Slide 1: Way forward on intra-cell interference scenarios for MUST
MediaTek, CHTTL, III, ITRI, ZTE
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th – 29nd May 2015
Agenda item 6.2.7.1
R1-153441

## Slide 2: Background
The following were agreed in last meeting:
  The same precoder for the superposed UEs is considered.
    The case when rank1 precoder vector for UE1 is v1,1 and rank2 precoder matrix for UE2 is [v2,1 v2,2] and v1,1 = v2,1 is also considered as the same precoder case.
    Although this does not preclude different precoder case, companies should provide detailed assumption for different precoder case, e.g., availability of the other UE’s precoder information and receiver assumptions, etc

## Slide 3: Proposals
  N-Tx eNB supports up to N spatial layers within a cell
  For generalization, the case when rank-K1 precoder matrix for UE1 is [v1,1, …, v1,K1] and rank-K2 precoder matrix for UE2 is [v2,1, …, v2,K2] and {v1,a1 = v2,b1, … , v1,aK = v2,bK}, where 1 ≤ aj ≤ K1, 1 ≤ bj ≤ K2 and K ≤ min(K1, K2), is considered as using the same spatial precoding vector