## Slide 1: WF on contention for LAA UL transmission
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell,…
3GPP TSG RAN WG1 #81 R1-153537
Fukuoka, Japan
25th – 29th May 2015
Agenda item: 6.2.4.3
Document for decision

## Slide 2: Background
LAA design should ensure fair coexistence with other technologies
  A STA can skip LBT and transmit in response to an AP transmission based on the Reserve direction grant protocol in Wi-Fi.
  The IEEE 802.11ax TG has recently approved the following motion on UL OFDMA operations:
    An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP.

## Slide 3: Proposal
LAA supports the following for UL transmission containing PUSCH:
  UL transmission with LBT at the UE.
  UL transmission without LBT at the UE when the UL transmission burst from the UE being served by an eNB follows within X microsecond after a DL transmission burst from that eNB
    X should be comparable with the DIFS and AIFS periods in Wi-Fi
    The total duration of DL and UL transmission bursts falls within the maximum channel occupancy time.