## Slide 1: WF on PRACH CE starting level
Huawei, HiSilicon, InterDigital, ALU, ASB, Qualcomm, Samsung,Panasonic,Intel,MediaTek, KDDI,ZTE
R1-153545
3GPP TSG RAN WG1 #81
Fukuoka, Japan, May 25-29, 2015
Agenda item 6.2.1.6

## Slide 2: Background
From LS to RAN4 in R1-150920 (RAN1#79):
“RAN1 is considering several approaches for selecting a starting PRACH repetition level. One approach is based on RSRP measurement, and another approach is based on RSRP measurement and PSS/SSS detection time. Some other approaches do not require RSRP measurements. RAN1 requests RAN4 to feedback on the possibility of distinction among non-coverage enhancement and coverage enhancement of max. 3 non-zero levels (e.g., 0, 5, 10, 15 dB, or 0, 6, 12, 18 dB, dB number is total system coverage enhancement), for example, using RSRP measurement depending on coverage level.”

## Slide 3: Proposal
UE determines based on RSRP measurement whether or not to operate PRACH CE
NOTE: RAN1 will re-visit after RAN4 conclusion: if a UE operating CE selects based on DL measurement a starting PRACH repetition level