## Slide 1: WF on LAA UL LBT
Intel, Ericsson, ETRI
3GPP TSG RAN WG1 #81 R1-153565
Fukuoka, Japan
25th – 29th May 2015
Agenda item: 6.2.4.3
Document for decision

## Slide 2: Background
Not only required by regulations in some regions, e.g., EU, UL LBT can improve the system performance by reducing collisions as shown by evaluation results from different companies.
In Wi-Fi (excluding 802.11ax), each of transmitters, regardless of DL AP or UL STA, contends the channel as one node.
By contrast, eNB scheduling based LAA UL transmission can substantially reduce the number of contending nodes since only the scheduled UEs are contending the channel in the UL.
It is observed by some companies’ simulation results that if the same LBT is required to both the eNB (prior to sending a UL grant) and the scheduled UE (prior to sending the scheduled PUSCH), the LAA UL performance can be significantly poor, especially when the LAA network coexists with a Wi-Fi network.
LAA design should ensure fair coexistence with other technologies
  A STA can skip LBT and transmit in response to an AP transmission based on the Reserve direction grant protocol in Wi-Fi.
  The IEEE 802.11ax TG has recently approved the following motion on UL OFDMA operations:
    An UL MU PPDU (MU-MIMO or OFDMA) is sent as an immediate response (IFS TBD) to a Trigger frame (format TBD) sent by the AP.

## Slide 3: Proposal (1)
LAA supports UL LBT.
    The UL LBT scheme can be different from the DL LBT scheme.
    If a UL grant is subject to LBT, for the UL LBT applied to the transmission scheduled by the grant
      The CCA ED threshold can be higher than that applied to the DL LBT for DL transmission burst containing PDSCH
      The contention window size can be smaller than that applied to the DL LBT for DL transmission burst containing PDSCH
      The LBT procedure can be simplified compared to that for the DL transmission burst containing PDSCH.
        Method 1: Only initial CCA for the UL LBT
        Method 2: No adaptation of the contention window size
        Other methods including a combination of the identified methods are not precluded.
      Other methods including a combination of the identified methods are not precluded.
The DL LBT schme for UL grant pcan be different from that for DL burst transmission containing PDSCH.

## Slide 4: Proposal (2)
In addition to UL LBT, it is recommended to consider the following:
  The eNB indicates to the UE not to perform LBT before transmission when the UL transmission burst occur within X microseconds after the DL transmission burst from that eNB on the same carrier
    X should be as comparable to SIFS
  Such a mode of operation is only allowed when the duration between the start of the DL transmission burst and the end of the UL transmission burst is less than the maximum channel occupancy time.