## Slide 1: WF on Narrowband Definition for Rel-13 MTC UEs
Huawei, HiSilicon
R1-153567
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th-29th, May 2015
Agenda item 6.2.1.1

## Slide 2: Proposal
A narrowband is defined as a set of contiguous PRBs
  Defined in the same way for both UL and DL
  NOTE: This avoids additional retuning in TDD
Narrowbands are non-overlapping
  Depending on the definition option, some PRBs may not be included in any narrowband
    FFS the location of these PRB(s) (e.g., edge(s), near the center, …)
  Depending on the definition option, the PSS/SSS/PBCH may be in one or more narrowbands

## Slide 3: Option 1
For even system BW, a narrowband is 6 PRBs
For odd system BW:
  Option 1A: The center narrowband is 5 PRBs, all other narrowbands are 6 PRBs
    5 PRB narrowband cannot support M-PDCCH with AL 24 or MTC SIBs requiring 6 PRBs
    15PRB system BW not supported as overlapping is not supported
  Option 1B: All narrowbands are 5 PRBs
    5 PRB narrowband cannot support M-PDCCH with AL 24 or MTC SIBs requiring 6 PRBs
  Option 1C: The center narrowband is 6.5PRBs, all other narrowbands are 6 PRBs
    From any narrowband (including the center), the UE will retune to receive PSS/SSS/PBCH

## Slide 4: Option 2
  A narrowband is 6 PRBs defined continuously starting from one edge of the system BW
    FFS if an offset is allowed for aligning UL narrowbands with legacy PUCCH and/or PRACH

## Slide 5: Unused PRBs
System BW | 100 | 75 | 50 | 25 | 15 | 6
Option 1A | 10 (=2x5) | 10 (=2x5) | 8 (=2x4) | 8 (=2x4) | 10 (=2x5) | 0
Option 1B | as 1A | 0 | as 1A | 0 | 0 | 0
Option 1C | as 1A | 8.5 (=2x4+.5) | as 1A | 6.5 (=2x3+0.5) | 8.5 (=2x4+.5) | 0
Option 2 | 4 | 3 | 2 | 1 | 3 | 0