## Slide 1: WF on Valid subframes for a PDSCH bundle transmission
LG Electronics,
R1-153575
3GPP TSG RAN WG1 #81
Fukuoka, Japan, 25th-29th, May 2015
Agenda item 6.2.1.3

## Slide 2: Proposals
When a UE is scheduled with a PDSCH bundle with ‘m’ repetition number
  A UE assumes that ‘m’ subframes would carry the PDSCH bundle over M subframes where M >= m
  A set of subframes which can be used for ‘m’ repetition of a PDSCH bundle is known to the UE
    A UE assumes that at least the following subframes would not be used for a PDSCH bundle
      Subframe(s) which can carry PMCH
        In case a subset of MBSFN subframe can be used for a PDSCH bundle, the set of fake-MBSFN subframes is known to UE via semi-static signaling
        FFS whether CFI and CRS mapping of a fake-MBSFN subframe is different from a normal subframe for Rel-13 LC UE
        FFS on exact signaling details
      Special subframes when special subframe configuration 0 or 5 is used in normal CP (0 or 4 in extended CP)
        Special subframe configuration is signaled by MTC SIB-1
      Uplink subframes in TDD
        DL/UL configuration is signaled by MTC SIB-1
      FFS on subframe(s) assumed to be used for frequency retuning when frequency hopping occurs in every Y subframes
      FFS on subframe(s) configured for a measurement gap
      FFS on other cases