## Slide 1: WF on observations on CSI enhancements
CATT, Intel, Ericsson, Qualcomm, Samsung
Agenda: 6.2.5
3GPP TSG RAN WG1 Meeting #81
Fukuoka, Japan, 25th - 29th May 2015
R1-153621

## Slide 2: Observation: beamformed CSI-RS based schemes
Observations for beamformed CSI-RS based enhancements:
  Increased CSI-RS coverage may be achieved by using FD MIMO beamforming
  Existing NZP-CSI-RS resources, codebooks and PUCCH formats may be reused to support FD MIMO
  May support different FD MIMO antenna shapes at the eNB including TXRUs > 64
  May support FD MIMO beamforming for rank > 2
  Similar UE complexity for CSI measurements may be maintained

## Slide 3: Observation: non-precoded CSI-RS based schemes
Observations on non-precoded CSI-RS based enhancements:
  3D MIMO channel measurements for CSI is available at the UE, i.e. all eNB antennas or ports can be measured at each UE antenna
  LTE implicit CSI feedback framework can be extended to support FD MIMO without new PUCCH formats
  High rank SU-MIMO is supported by codebook design
  Implicit CSI feedback is sufficient for the eNB to determine DL precoder.
  Similar UE complexity for CSI calculation may be maintained by codebook design.

## Slide 4: Observation: hybrid CSI-RS based schemes
Observations for hybrid CSI-RS based schemes:
  CSI-RS overhead reduction for larger number of TXRUs
  Facilitate determining the beamforming weight for beamformed CSI-RS