## Slide 1: Motivation for flexible framework for non-precoded CSI-RS
Agenda Item 6.2.5.2.3
3GPP TSG RAN WG1 #81 R1-153586
Fukuoka, Japan, 25th – 29th May 2015

## Slide 2: Background
SI on FD-MIMO is concluding with two main modes of operation identified:
  Non-precoded CSI-RS (codebook based feedback as in Rel.12)
  Beamformed CSI-RS
The number of TXRU is an eNB implementation issue,
  the use of the number of TXRU in RAN1 was introduced to align the simulation results in the SI

## Slide 3: Current eNB antennas
Current eNB has typically 2,5,6,9,10,14 or 20 rows of antenna elements (see examples on next page)
  The number of rows has been “hidden” in Rel.8-12 since only one dimensional precoding feedback is assumed.
    With FD-MIMO, this changes, as channel from both rows and columns of antenna elements are measurable
  Antenna design need to meet many requirements (e.g. antenna gain, multi-band, heat dissipation, size/volume/weight, grating lobes, steering angle range, ….)
  The more elements the higher gain, so the antenna designers tend to fit as many elements as possible into the constrained volume.
    If this needs to be a power 2 number, it will (most likely) cost antenna gain

## Slide 4: Examples of existing x-pol antennas of today

## Slide 5: FD-MIMO flexibility
If FD-MIMO specification is restricted to 1,2,4,8 ports per row/column, FD-MIMO feature would be less attractive
  Antenna design becomes difficult due to these constraints
  It may be hard to fulfill requirements, leading to inefficient designs
  The actual size (and weight) of the antenna is usually constrained by tower construction, wind load, permits etc, and if an antenna is replaced by a new with different characteristic (size, weight, etc) new negotiations with landlords, tower owners and local authorities is needed