## Slide 1: WF on Handling of Subframes Unavailable for Repetition
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Qualcomm, Sequans, Verizon, AT&T, Gemalto
R1-154822
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.1

## Slide 2: Proposal
Handling of subframes not available for repetition
  Postpone repetitions till the next available subframe in case unavailable subframes are known cell-wide, e.g., due to TDD, MBSFN, PRS subframe
    This is in line with the TDD behaviour of Rel-8 PUSCH TTI bundling and Rel-8 PUCCH HARQ-ACK repetition
    FFS: Before receiving SIB1, the UE does not know the TDD configuration  assume worst case TDD configuration when receiving MTC-SIB1
    FFS: Before receiving SIB2, the UE does not know the MBSFN configuration  assume worst case MBSFN configuration when receiving MTC-SIB1/SIB2
  Drop repetitions in case the unavailable subframes are UE-specific, e.g., due to measurement gap