## Slide 1: WF on LAA Energy Detection Threshold
Cisco, Broadcom, CableLabs
3GPP TSG RAN WG1 #82 R1-154827
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Thresholds for LAA Uplink
For LAA UL, network shall configure energy detection threshold at an LAA UE between a lower limit X <= -77 dBm and an upper limit -62 dBm
  Reference on X = -77 dBm is based on IEEE submission to LAA workshop [802.19-15/0069r7]
  FFS on details on whether/how to adapt the UE’s energy detection threshold based on presence of Wi-Fi.

## Slide 3: Thresholds for LAA Downlink
LAA eNB shall use an Energy Detection Threshold between X and -62 dBm
  When LAA senses co-channel Wi-Fi, Energy Detection Threshold shall be set to X dBm
    FFS sensing procedure for determine presence of co-channel Wi-Fi which is used to adapt the threshold
  X is recommended at -77 dBm based on contributions from Cisco [R1-153339] and Broadcom (R1-152937).
Notes:   Note: Method for sensing co-channel Wi-Fi is FFS.
  Two potential methods are:
Wi-Fi transmission detection at eNB
UE feedback of detected Wi-Fi transmission