## Slide 1: Discussion on V2X Fast Fading Modeling based on Field Measurements
Ericsson
AI 7.2.8.1.1
R1-154833
3GPP TSG RAN WG1 Meeting #82

## Slide 2: Field Trial Results at 5.9GHz
“Cooperative Intelligent Transport Systems: Field Trials at 5.9GHz” – P.Alexander, D.Haley, A.Grant, IEEE 2011, (invited paper)
  Extensive measurement results in several countries (3 years, 35 trials, 1100km..)
Results provided for urban LoS/NLoS and highway LoS/NLoS

## Slide 3: Results from Field Trials: Delay Spread
RMS Delay spread quantiles:
EPA and UMi LoS have appropriate PDP
  Umi NLOS PDP can also used as challenging (not worst case) scenario
EPA
EPA
EVA
EVA
2510
UMi LoS
UMi NLoS
UMi NLoS
UMi LoS

## Slide 4: Results from Field Trials: Doppler Spread (1)
RMS Doppler spread scatter plots
Key message: no correlation between Doppler spread and delay spread
This is NOT reflected by the modified CDL model in TR 36.843!

## Slide 5: Results from Field Trials: Doppler Spread (2)
Relative speed is not proportional to RMS Doppler spread
  Again, the modified CDL model in TR 36.843 is inaccurate because it uses relative speed

## Slide 6: Results from Field Trials: Doppler Spread (3)
From the reference paper:
…
It seems natural to model Doppler spread based on the combination of UEs absolute speeds rather than relative speed Note: effective speed = sqrt(v1^2+v2^2)

## Slide 7: Proposal
For both link and system simulations, fast fading is modeled according to:
  PDP of EPA (Umi NLOS as optional PDP)
  Each EPA tap is an independent process with modified Jakes spectrum (dual mobility using abs(v1) and abs(v2))
    Modified Jakes described by NEC (R1-132341) and captured in TR 36.843
    The modified Jakes spectrum can be implemented in any way. Efficient implementations based on SoS described e.g. in [Patel, Stuber, Pratt, “Simulation of Rayleigh-Faded Mobile-to-Mobile Communication Channels”, IEEE Trans. On Comm., Nov. 2005]