## Slide 1: WF on UE support of carrier selection
Huawei, HiSilicon, Samsung, Sony
3GPP TSG RAN WG1 #82 R1-154896
Beijing, China
24th – 28th August 2015
AI: 7.2.4.3

## Slide 2: Background
Terminologies
  Carrier selection: The selection of a subset of carriers available at the network, performed by the eNB;
  Carrier switching: The switching from one carrier to another carrier, performed by the UE as instructed by the eNB.
Without UE supporting CA of all available carriers at the eNB, carrier selection may not be useful due to long delay (from RRC signaling and MAC activation/deactivation) before UE can utilize the selected carrier(s)

## Slide 3: Proposal
Semi-static carrier switching with enhanced SCell configuration is supported. The standards impacts include:
  Configuring the UE with a number of carriers potentially exceeding the maximum number of carriers over which the UE can aggregate PDSCH
  RRM measurements over the configured carriers
Fast carrier switching is supported at least for LAA. The standard impacts include:
  L1 indication to the UE to start monitoring a carrier, which is selected from the configured carriers by the eNB