## Slide 1: WF on subframes with MBSFN structure in LAA
Qualcomm, …
3GPP TSG RAN WG1 #82 R1-154901
Beijing, China
24th – 28th August 2015
Agenda item: 7.2.4.1
Document for decision

## Slide 2: Background
Need for MBSFN subframes
  LAA may support both CRS and DMRS based TMs
  In current LTE, subframes with CRS in first symbol (subframes having MBSFN structure) can be used for DMRS based transmission without CRS overheard thus increasing transmission efficiency.
Number of configured subframes
  Currently, the MBSFN configuration is semi-static RRC based and up to 60% of subframes can be configured as MBSFN subframes
  Rel-13 LAA only supports DL transmission and cannot be configured as Pcell/PScell. eNB serving UEs using DMRS based modes may want to all the subframes as MBSFN subframes in a transmission burst
  We propose to increase the number of subframes that can have MBSFN from the current 60% in LTE

## Slide 3: Proposal
LAA supports subframes with CRS transmission only in the first symbol (2 symbols in case of 4 port CRS) similar to subframes with MBSFN structure
  FFS partial subframes
On LAA carriers, the number of subframes having such an MBSFN structure can be up to X% of all subframes
  X is more than 60, FFS exact value of X