## Slide 1: WF on Scenario for V2x
NTT DOCOMO, CMCC, Vodafone
R1-154906
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.8.1.1

## Slide 2: Proposal 1
Following RAN aspects for PC5-based V2V operation (Tx/Rx of V2V message) are captured in the TR
(Aspect 1) Operation bands used as test points for evaluation
  Case 1A: 6 GHz
  Case 1B: 2 GHz
  Note: Case 1B may not be need to be specifically simulated for all scenarios
(Aspect 2) eNB deployment including possibility of network control
  Case 2A: UE autonomous resource allocation, at least mode 2, based on semi-statically network-configured/pre-configured radio parameters.
  Case 2B: eNBs providing more UE specific or/and more dynamic resource allocation compared to case 2A.
  Note: Related to aspect 2, it is necessary to consider the condition to apply any preconfigured radio parameters.
  Note: The following case is categorized as in-coverage: a UE can access eNB on a LTE carrier and receive radio parameters for PC5 transport on another carrier (e.g., 6 GHz).
(Aspect 3) Multi-carrier operation
  Case 3A: UEs communicating over PC5 across a single carrier.
  Case 3B: UEs communicating over PC5 across multiple carriers.
(Aspect 4) Multi-operator scenarios
  Case 4A: Single operator for PC5 operation.
  Case 4B: A set of PC5 operation carrier(s) is shared by UEs subscribed to different operators. This means that UEs belonging to different operators may transmit on the same carrier.
  Case 4C: Each operator is allocated with a different carrier. This means that a UE transmits only on the carrier allocated to the operator which it belongs to.
(Aspect 5) Co-existing with Uu
  Case 5A: Dedicated carrier for V2x. There is no uplink (Uu) traffic on the PC5 operation carrier.
  Case 5B: V2x carrier is shared with Uu.

## Slide 3: Proposal 2
All scenarios and combinations captured in slide 2 should be considered in scope of the study item.
For initial evaluations for PC5 based V2V in RAN1, following scenario is proposed to simulate as a starting point for evaluation simplicity.
  Case 1A: 6 GHz band
  Case 2A: Rel-12 mode 2 resource allocation
  Case 3A: and 5A: Single dedicated carrier for V2V
  Case 4A: Single operator
Total resource required to serve required V2V vehicle density should be verified: i.e. required amount of time-frequency resource for V2V should be an output metric of the simulation.
If capacity optimization is identified as needed in the study, enhancements to D2D resource allocation and/or multi-carrier operation could be considered to understand gains.