## Slide 1: WF on remaining issues of Narrowband definitions
NEC,LGE, Intel, InterDigital, CATT, Samsung
3GPP TSG RAN WG1 Meeting #82
Beijing, China, August 24 – 28, 2015
Agenda Item: 7.2.1.1
R1-154909

## Slide 2: Background
Agreement at RAN1#80bis:
  A set of DL and UL narrow-band(s) are known to UE
    Definition of narrow-band(s) is specified in the spec
      FFS details of a definition of narrow-band(s)
    FFS on how to UE knows available narrow-band(s) for MTC UEs
  One narrow-band size is 6PRB
    FFS on other narrow-band size(s)
  PRBs in a narrow-band are aligned with legacy PRB mapping
  Frequency hopping over the system bandwidth is not used for at least
    PSS/SSS
    PBCH
  At least in CE, frequency hopping over the system bandwidth can be used for common message for Rel-13 MTC UEs (RAR, paging, MTC SIB(s), FFS on response for message 3)
  Hopping pattern between narrow-bands is supported
    FFS on details of hopping pattern

## Slide 3: Background
Agreement at RAN1#81:
A narrowband is defined as a set of contiguous PRBs
  At least for TDD, the same set of narrowbands are specified for both DL and UL
  NOTE: This avoids additional retuning in TDD
Narrowbands are non-overlapping
  FFS: Some PRBs may not be included in any narrowband
    FFS the location of these PRB(s) (e.g., edge(s), near the center, …)
  The PSS/SSS/PBCH may be in one or more narrowbands. PSS/SSS/PBCH is independent of any narrowbands
    In case a UE needs to monitor PSS/SSS/PBCH of a cell, it can be retuned to the center 72 subcarriers (excluding system DC)
FFS how the narrowbands are defined across the system BW
FFS if an offset is allowed for aligning UL narrowbands with legacy PUCCH and/or PRACH

## Slide 4: Proposal
Total number of DL narrowbands 6-RBs size in the system bandwidth is
Total number of maximum UL narrowbands 6-RBs size in the system bandwidth is
  FFS: Offset is allowed for aligning UL narrowbands with legacy PUCCH and/or PRACH
FFS whether partial narrowband is defined for the remaining RBs if any
The location of the remaining RBs if any is FFS between
  A) The remaining RBs are at the end of the system bandwidth
  B) The remaining RBs are in the middle of the system bandwidth
The numbering of narrowbands is FFS between:
  Narrowbands are numbered in order of increasing PRB number
  Narrowbands are numbered working from the edges of the system bandwidth to the middle

## Slide 5: For Reference