## Slide 1: WF on Cross-subframe Channel Estimation for PDSCH
Ericsson, Sequans, Samsung, InterDigital, Intel, Sony, Sierra Wireless, CATT, LGE, Nokia Networks, Lenovo, ZTE
R1-154973
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.3

## Slide 2: Background (1)
Agreements:
  For Rel-13 low complexity UE in enhanced coverage, the following techniques related to at least unicast PDSCH should be supported
    In order to allow cross-subframe channel estimation, PRB position is the same during at least X subframes
      X value and configuration are FFS
      This does not preclude dis-continuous transmission for unicast PDSCH
    Frequency hopping is supported over the system BW
      If/when frequency hopping is applied, frequency location should be switched every Y consecutive subframes, where Y is equal to or larger than X, assuming re-tuning time is included in Y.
      Configurability is FFS
    FFS: Other techniques

## Slide 3: Background (2)
Agreements:
  For the physical downlink control channel repetition for Rel-13 low-complexity MTC UEs in enhanced coverage, the following techniques are supported
    In order to allow cross-subframe channel estimation, location of a PRB-set for physical downlink control channel for MTC is the same during at least X subframes
      X value and indication are FFS
      This does not preclude dis-continuous transmission for the physical downlink control channel for MTC
      Working assumption: Same precoding matrix is assumed per antenna port and at least one PRB for at least X subframes
    Frequency hopping is supported over the system BW
      If/when frequency hopping is applied, frequency location is switched according to a pattern every Y consecutive subframes, where Y is equal to or larger than X, assuming re-tuning time is included in Y
      Configurability of X, Y, and frequency hopping is FFS

## Slide 4: Proposal
When frequency hopping is configured for the PDSCH with DMRS-based transmission ,
  Same precoding matrix is assumed per antenna port at least on the same PRB for at least X consecutive subframes
  Precoding matrix may vary from one set of X subframes to another set of X subframes
  X is the number of consecutive subframes where PDSCH is transmitted in the same narrowband (excluding retuning time)
  This does not preclude dis-continuous transmission of the PDSCH
FFS: When frequency hopping is not configured for the PDSCH