## Slide 1: WF on PRACH transmit power
Huawei, HiSilicon, Intel, InterDigital, Samsung, Panasonic
R1-154980
3GPP TSG RAN WG1 #82
Beijing, China, August 24-28, 2015
Agenda item 7.2.1.6

## Slide 2: Background (1)
The following FFS point remains since RAN1#80:
  For coverage enh. of PRACH, for initial random access:
    ….
    FFS: Power ramping or always max power used within each repetition level
Up to 3 PRACH repetition levels can be configured, spanning up to 17 dB PRACH coverage enhancement

## Slide 3: Background (2)
PRACH transmit power, PPRACH, is set according to:
PREAMBLE_RECEIVED_TARGET_POWER = preambleInitialReceivedTargetPower + DELTA_PREAMBLE + (PREAMBLE_TRANSMISSION_COUNTER – 1) * powerRampingStep
preambleInitialReceivedTargetPower : configured by RRC
DELTA_PREAMBLE: Difference between preamble formats
PREAMBLE_TRANSMISSION_COUNTER: Number of attempts so far
powerRampingStep: Power ramping level for each attempt
PPRACH = min{ PCMAX,c(i), PREAMBLE_RECEIVED_TARGET_POWER + PLc }
The parameters are configured from higher layers
See TS 36.213 and TS 36.321

## Slide 4: Proposals
PRACH power ramping procedure within each repetition level is based on current PRACH transmit power equation.
After UE changes to next higher repetition level, PREAMBLE_RECEIVED_TARGET_POWER is adjusted from the previous repetition level attempt transmit power.
  The difference in the number of repetitions is taken into account.
    NOTE: whether CDM is applied or not is network implementation. It is allowed not to use CDM between PRACH repetition levels with large differences in amount of CE.
    FFS: Transmit power of the other random access procedure messages