## Slide 1: WF on MTC-SIB1 frequency hopping
Ericsson, CATT, ETRI, Huawei, HiSilicon, Intel, InterDigital, LG Electronics, Marvell, NEC, Nokia Networks, NTT DoCoMo, Panasonic, Qualcomm, Samsung, Sequans, Sierra Wireless, Sony
R1-154864
3GPP TSG RAN WG1 Meeting #82
Beijing, China, 24th - 28th August 2015
Agenda item 7.2.1.1

## Slide 2: Proposal
Confirm working assumption: At least in case the network supports enhanced coverage, frequency hopping for MTC-SIB1 is always used at least system bandwidth >= 5MHz.
  Option A: MTC-SIB1 frequency hopping takes place between 2 narrowbands in the cell.
  Option B: MTC-SIB1 frequency hopping takes place between 2 or 4 narrowbands as indicated in MIB.
  Working assumption: The mentioned narrowbands are determined based on cell ID and system bandwidth.
  Working assumption: The hopping sequence between these narrowbands is determined based on cell id and subframe index (and/or SFN).