## Slide 1: WF on AI 7.2.1.5 PUCCH and UCI
Ericsson
R1-156325
3GPP TSG RAN WG1 Meeting #82bis
Malmö, Sweden, 5th - 9th October 2015
Agenda item 7.2.1.5

## Slide 2: Summary
Proposal 1 and Proposal 4 have gathered substantial support
  PUCCH resource determination for LC/CE UEs [Ericsson, MediaTek, Qualcomm, Intel, Panasonic, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Sequans, Verizon Wireless]
  CSI and CQI for MTC [Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Qualcomm, Sequans, Verizon Wireless, LGE, DoCoMo]

## Slide 3: Proposal 1
PUCCH resource determination for LC/CE UEs [Ericsson, MediaTek, Qualcomm, Intel, Panasonic, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Sequans, Verizon Wireless]
LC UEs and UEs operating CE derive PUCCH resources for HARQ ACK/NACK using legacy principle
  That is, implicitly from lowest ECCE index of the corresponding M-PDCCH transmission.
  Explicit PUCCH resource configuration by RRC (as in LTE Rel-12) is also supported.
In case of PUCCH repetitions, the same PUCCH resources are used within each subframe of a PUCCH bundle.
The narrowband regions indicated by MTC SIB for PUCCH can be common for all CE levels

## Slide 4: Proposal 2
ACK/NACK Bundling Support for HD-FDD LC UEs [Sierra, Sony, CATT, Sequans, …]
For at least HD-FDD Rel-13 low complexity UEs operating without repetition, ACK/NACK bundling shall be supported.
  The design will be based as closely as possible on the TDD ACK/NACK bundling design
  ACK/NACK bundling will be configured by RRC
  4 ACK/NACK bundling will be supported
  FFS: if 8 ACK/NACKs will be supported
  FSS: how invalid SFs will be handled

## Slide 5: Proposal 3
Periodic CSI feedback [ZTE, …]
For Rel-13 MTC UE in normal coverage
  Subband CQI reporting is supported
    FFS details reporting configuration
  Wideband CQI reporting is supported
    Wideband CQI is the average CQI measurement over narrowbands monitored by a MTC UE
For Rel-13 MTC UEs in normal coverage, choose between the following options for CSI measurement:
  Option 1: Define measurement gap for CSI measurement. During the measurement gap, UE measures the predefined narrowbands and stops the detection of M-PDCCH and PDSCH
    In the case the predefined narrowbands overlap with the narrowband where M-PDCCH/PDSCH is located, UE continues detection of M-PDCCH/PDSCH on that narrowband
  Option 2: UE measures the narrowband where M-PDCCH/PDSCH is located

## Slide 6: Proposal 4
CSI and CQI for MTC [Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Qualcomm, Sequans, Verizon Wireless, LGE, DoCoMo]
The number of subframes M (>1) that CSI reference resource spans is predefined or implicitly derived from CE level.
Existing CQI table is extended with new CQI entries for LC/CE UEs.
The new CQI entries provide lower spectral efficiency values corresponding to repetitions across multiple subframes.

## Slide 7: Proposal 5
PUCCH Configuration Info Optionally Carried by RAR [MediaTek, …]
PUCCH resources for Msg4 feedback is optionally carried in MAC RAR if the implicit PUCCH configuration can’t avoid resource collision.