## Slide 1: Summary on CSI-RS Enhancement for Class A Reporting
Samsung
3GPP TSG RAN WG1 #83 R1-157546
Anaheim, USA, 15th - 22th November 2015
Agenda item: 6.2.4.2.1

## Slide 2: CDM-2 Details
(N,K) for resource aggregation for CDM-2
  For 16 ports
    (N,K)=(8,2) supported by 7 companies (Samsung, Huawei, CATT, NEC, ETRI, E///, LGE)
    (N,K)=(2,8) supported by 3(+1) companies (Samsung, CATT, E///, (QC))
  For 12 ports
    (N,K)=(4,3) supported by 7 companies (Samsung, Huawei, CATT, NEC, ETRI, E///, LGE)
    (N,K)=(2,6) supported by 3(+1) companies (Samsung, CATT, E///, (QC))

## Slide 3: CDM-4 Details
Alternatives for CDM-4 RE mapping
  Alt.1: CDM-T
    Supported by 6 companies: Samsung, E///, NEC, LGE, DOCOMO, ETRI
  Alt.2: CDM-TF (adjacent subcarriers)
    Supported by 7(+1) companies: E///, LGE, QC, (Nokia), DOCOMO, Huawei, Intel, ZTE
  Alt.3: CDM-TF (apart by 6 subcarriers)
    Supported by 5 companies: Samsung, E///, DOCOMO, Intel, ZTE
  Alt.4: CDM-TF (apart by 2 subcarriers)
    Supported by 1 company: NEC

## Slide 4: CDM-4 Details
(N,K) for resource aggregation for CDM-4
  For 16 ports
    (N,K)=(8,2) supported by 5 companies: Samsung, Huawei, ZTE, ETRI, E///
    (N,K)=(4,4) supported by 2(+2) companies: Samsung, LGE, (DOCOMO, can consider), (E///, conditional)
    (N,K)=(2,8) supported by (2) companies: (DOCOMO, can consider), (E///, conditional)
  For 12 ports
    (N,K)=(8,2) supported by 3 companies: ZTE, ETRI, Samsung
    (N,K)=(4,3) supported by 4(+2) companies: Samsung, Huawei, ZTE, LGE, (DOCOMO, can consider), (E///, conditional)
    (N,K)=(2,6) supported by 1(+2) companies: CATT, (DOCOMO, can consider), (E///, conditional)
Other proposals for CDM-4 RE mapping
  9th and 10th OFDM symbol only (supported by Intel, QC, Huawei)
  Define a new sequence rule for CDM-4 (supported by Nokia)
  Define a new CSI-RS resource configuration table for CDM-4 (supported by LGE)

## Slide 5: Port numbering
For CDM-2
  Alt.1: Support FFS in RAN1#82bis working assumption (Samsung, CATT, LGE, Intel)
    The port numbers in the aggregated resource is given by n=(k-1)*N+p, p = 15,…,14+N
  Alt.2: Define new numbering rule (ZTE, NEC, E///, CMCC)
For CDM-4, most companies seem to have considered:
  The CDM-4 RE quadruplet corresponds to two pairs of CDM-2 REs whose ports are numbered according to the respective alternatives above.
where k = 0,…,K-1 is the kth aggregated resource and N is the number of ports per aggregated resource

## Slide 6: Other proposals
1 PRB pair based CSI-RS configuration
  Supported by 2 companies: Huawei, NEC