## Slide 1: WF on Regulation and MCOT
Ericsson, Intel, CATT,…
3GPP TSG RAN WG1 #83 R1-157555
Anaheim, USA, 15th - 22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background
The recommendation in section 9.19.3.3 in IEEE specification [1] states
  “In certain regulatory domains, channel sensing needs to be done at periodic intervals (for example, in Japan, this period is 4 ms). This means that the duration of a TXOP in these regulatory domains might not be more than this periodic interval. If longer durations are desired, then the TXOP holder needs to sense the channel at least once in the limit imposed in the regulatory domain, by waiting for at least for the duration of one PIFS during which it senses the channel. If it does not detect any energy, it may continue by sending the next frame. In other words, the total TXOP size assigned should include an extra time allocated (i.e., n × aSlotTime, where n is the number of times the STA needs to sense the channel and is given by Floor(TXOP limit/limit imposed in the regulatory domain). 34The TID value in the QoS Control field of a QoS Data+CF-Poll frame pertains only to the MSDU or fragment thereof in the Frame Body field of that frame. This TID value does not pertain to the TXOP limit value and does not place any constraints on what frame(s) the addressed STA may send in the granted TXOP.”
[1] IEEE Std 802.11-2012, Part II: Wireless LAN MAC and PHY Specifications
4ms
1ms
Access after successful random backoff
Channel is released due to 4ms req.
Channel is sensed to be idle for PIFS duration.
Channel is released due to TXOP limit.
Example TXOP limit =5ms +PIFS

## Slide 3: Proposal
Where the regulations require channel sensing at periodic intervals (for example in Japan this period is 4ms), the eNB can sense the channel to be idle for a single continuous interval of duration 25 µs when the DL transmission burst meets the limit imposed by the regulation before continuing its transmission within the maximum channel occupancy time.
Note: The European regulation requires full LBT procedure corresponding to the equipment type when the DL transmission burst meets the limit imposed by the regulation.