## Slide 1: Proposal on power-control for the new PUCCH formats
NTT DOCOMO, INC.
R1-157561
3GPP TSG RAN WG1 #83
Anaheim, USA, 16th – 20th November 2015
Agenda item 6.2.2.1.1

## Slide 2: Proposal
RAN1 selects one of the two power-control equations described in the following slides.

## Slide 3: Option 1: Using DTF,c(i)
For the PUCCH format 4 and 5, following power-control formula is used.
  Where PO_PUCCH,c = PO_NORMIMAL_PUCCH + PO_UE_PUCCH with PO_UE_PUCCH being an integer (-8, …, 7) specifically configured for the PUCCH format, and
  DTF,c(i) = 10log10(21.25BPRE-1) with BPRE = OUCI/NRE.

## Slide 4: Option 2: Using h-function
For the PUCCH format 4 and 5, following power-control formula is used.
  Where PO_PUCCH,c = PO_NORMIMAL_PUCCH + PO_UE_PUCCH and PO_UE_PUCCH is an integer (-8, …, 7) commonly configured for all the PUCCH formats, and
  DF_PUCCH(F) is one of 8 PF-dependent power-offsets configured by higher-layer, and
  h(nCQI, nHARQ, nSR) = 10log10(nCQI + nHARQ + nSR + nCRC)