## Slide 1: WF on further PDSCH issues for eMTC
[Sony]

## Slide 2: Proposal on PDSCH Resource Block Type (Issue 1)
VRB of distributed type is not supported

## Slide 3: Proposal on PDSCH Resource Allocation Type (Issue 2)
Mode A: only resource allocation type 0 is supported.
Mode B: 6 PRB allocation is implicitly supported.

## Slide 4: Proposal on Case 2 PDSCH Scheduling (Issue 4)
For Rel-13 low complexity UEs operating in mode A, under cross-subframe scheduling, no case 2 is defined.
For Rel-13 low complexity UEs operating in mode B, under cross-subframe scheduling, case 2 is applied.
  For DL cross-subframe scheduling Case 2 without repetition and with repetition, PDSCH (new and re-transmissions) starts from the second valid downlink subframe after the end of the corresponding transmitted M-PDCCH with the given repetition level
In case of frequency hopping, retuning occurs within 2 OFDM symbols and there is no need for a retuning subframe

## Slide 5: Proposal on Number of DL / UL HARQ Processes (Issue 6)
In small coverage enhancement, the same number of DL and UL HARQ processes is supported as in the no coverage enhancement case.

## Slide 6: Proposal on PUCCH ACK / NACK Transmission (Issue 13)
Both ACK and NACK can be transmitted on PUCCH to indicate reception status of PDSCH.

## Slide 7: Proposal on Number of TDD HARQ Processes (Issue 5)
The number of TDD DL HARQ processes under cross-subframe scheduling in Mode A are as follows:
TDD UL/DL configuration | Maximum number of HARQ processes
0 | 6
1 | 9
2 | 12
3 | 11
4 | 14
5 | 16
6 | 8

## Slide 8: Proposal on PDSCH and PUSCH HARQ feedback collisions (Issue 10)
When PDSCH and PUSCH HARQ feedback collisions occur, downselect between the options:
  Option 1: collisions avoided by eNodeB scheduling or by UE implementation (no spec impact)
  Precedence rules defined in spec: either
    Option 2A: PDSCH prioritized over HARQ ACK / NACK
    Option 2B: HARQ ACK / NACK prioritized over PDSCH

## Slide 9: Proposal on Supported Number of Antenna Ports (Issue 11)
The number of antenna ports supported in DMRS modes can be different to the number supported in CRS modes and:
For CRS modes: the number of antenna ports supported by the UE is downselected between:
  Option 1: 2 antenna ports
  Option 2: 4 antenna ports
For DMRS modes, the number of antenna ports supported by the UE is downselected between:
  Option 1: 2 antenna ports
  Option 2: 4 antenna ports