## Slide 1: Discussion on Starting Subframe Set Configuration
LG Electronics
R1-157598
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.10

## Slide 2: Proposal
A cell-specific gap or gap index
  5 values of gap can be considered
    0 for 0 gap
    1 for 25% gap
    2 for 50% gap
    3 for 100% gap
    4 for 200% gap (is it necessary?)
  Single a cell-specific “gap” is used for all repetition numbers
  In FDD: Map repetition numbers {1, 2, 4, 8, 16, 32, 64, 128, 256} to set to
    Index 0: {1, 2, 4, 8, 16, 32, 64, 128, 256} (gap 0%)
    Index 1: {1, 5, 5, 10, 20, 40, 80, 100, 200, 400, 800} (gap 25%)
    Index 2: {1, 3, 6, 12, 24, 48, 96, 192, 396} (gap 50%)
    Index 3: {1, 4, 8, 16, 32, 64, 128, 256, 512} (gap 100%)
    Index 4: {1, 6, 12, 24, 48, 96, 192, 396, 798} (gap 200%)

## Slide 3: Proposal
  In TDD: Map repetition numbers {1, 2, 4, 8, 16, 32, 64, 128, 256} to a set according to configured gap index
    Configuration 0:
      Index 0: {1, 5, 10, 20, 40, 80, 160, 320, 640} (gap 0%)
      Index 1: {1, 10, 20, 40, 80, 160, 320, 640, 1280} (gap 100%)
    Configuration 1
      Index 0: {1, 5, 10, 20, 40, 80, 160, 320, 640} (gap 0%)
      Index 1: {1, 10, 20, 40, 80, 160, 320, 640, 1280} (gap 100%)
    Configuration 2
      Index 0: {1, 5, 5, 10, 20, 40, 80, 160, 320} (gap 0%)
      Index 1: {1, 5, 10, 20, 40, 80, 160, 320, 640} (gap 100%)

## Slide 4: Illustration

## Slide 5: Illustration

## Slide 6: Proposal
3 bits of a cell-specific gap/periodicity can be configured for starting subframe configuration for search space for M-PDCCH scheduling RAR and search space for M-PDCCH scheduling Msg 3 retx/Msg 4.
  FFS details on the set of gap/periodicity values and how it applies to each maximum R
  The same gap is used for USS starting subframe configuration as a default value.
  UE-specific RRC signaling of 3 bits of a gap can be configured for starting subframe configuration for USS