## Slide 1: WF on M-PDCCH Order (Higher layer impact)
LG Electronics...
R1-157599
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.7

## Slide 2: Proposal
Confirm the working assumption
  M-PDCCH order is supported in both CE mode A and in CE mode B
DCI sizes for M-PDCCH order
  In CE mode A: the same size to DCI M1A
  In CE mode B: the same size to DCI M1B
  Details are FFS
No additional RRC signaling is assumed to support M-PDCCH order
For PRACH repetition/CE level, the same CE level used in last successful PRACH transmission is assumed unless a CE level is indicated dynamically
  FFS whether to support dynamic indication of CE level
Starting subframe and repetition number for PRACH transmission is determined based on SIB PRACH resource configuration for the CE level
In CE mode A
  Both preamble index and mask index can be indicated dynamically via M-PDCCH order
In CE mode B
  Mask index are not dynamically indicated via M-PDCCH order
    PRACH resource index is determined based on SIB PRACH resource configuration for the CE level
  Preamble index can be dynamically indicated via M-PDCCH order
    FFS whether the size of preamble index is reduced

## Slide 3: DCI Example in CE mode A
DCI field | Field size for DL grant | Field size for M-PDCCH order | M-PDCCH order purpose
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | [ceil(log2(number of narrowbands))] | Set to 1’s | Used for differentiating between DL grant and M-PDCCH order
PRB assignment | [5 or 6] | Set to ‘1’s or ‘0’s depending on resource allocation type | Used for differentiating between DL grant and M-PDCCH order
Repetition number | 2 | 6 | Preamble index
MCS | 4 |  | 
RV | 2 | 4 | MaskIndex
TPC for PUCCH | 2 |  | 
NDI | 1 | reserved | reserved
HARQ process number | 3 for FDD 4 for TDD |  | 
SRS request | [0 or 1] |  | 
DAI | 0 for FDD 2 for TDD 0 for HD-FDD |  | 
HARQ-ACK resource offset | 2 |  | 
M-PDCCH repetition number | 2 | 2 | M-PDCCH repetition number

## Slide 4: DCI Example in CE mode B
DCI contents | Field size for DL grant | Field size for M-PDCCH order | M-PDCCH order purpose
UL/DL flag | 1 | UL flag | UL flag
Narrowband index | ceil(log2(number of narrowbands) +1) | Set to ‘1’s if narrowband index is used | Set to ‘1’s if narrowband index is used Used for differentiating between DL grant and M-PDCCH order
Repetition number | 3 | Set to ‘1’s | Set to ‘1’s Used for differentiating between DL grant and M-PDCCH order
MCS | 4 | 6 | Use for preamble index
HARQ process number | 1 |  | 
NDI | 1 |  | 
HARQ process number | 1 | 0 | Reserved
HARQ-ACK resource offset | [0 or 1 or 2] |  | 
M-PDCCH repetition number | 2 | Use for M-PDCCH repetition number | Use for M-PDCCH repetition number