## Slide 1: Way Forward on PDSCH/PUSCH Remaining Issues
Spreadtrum, NEC, Panasonic
R1-157604
3GPP TSG RAN WG1 Meeting #83
Anaheim, Usa, 15th – 22nd November 2015
Agenda item 6.2.1.4

## Slide 2: Background
PDSCH related simulations results are found in:
R1-157333, Discussion on open issues in MTC PDSCH, Spreadtrum Communications
R1-156683, Extending the scrambling sequence for DL/UL transmissions, NEC
R1-156945, eMTC PDSCH symbol level combining for CE mode B, Panasonic
Extending scrambling in long repetitions is providing significant performance improvement
Symbol level combining is also providing performance improvement

## Slide 3: Background
Agreement:
In case of PUSCH transmission from LC UEs and UEs operating coverage enhancement
  The redundancy version (RV) is cycled every Z subframes
    For no or small repetitions, Z=1
      FFS whether or not a TB can be mapped to X>1 subframes as a bundle
        Value of X FFS
    Otherwise, Z>1
      The scrambling sequences at least for PUSCH data are the same in the same Z subframes
      Z is not explicitly configured
      FFS the value of Z
  The RV cycling follows legacy RV cycling pattern i.e. RV {0,2,3,1}

## Slide 4: Proposal
  For PDSCH transmission, RV value is cycled every Z subframes where Z=1 for CE Mode A and Z>1 for CE Mode B.
    In CE Mode A, RV value applied in the first subframe for PDSCH transmission is indicated by DCI.
  PDSCH/PUSCH data and PDSCH DMRS scrambling sequences are different in every Z subframes for duration of repetitions
    FFS: Actual method to initialize the scrambling sequence generator for each Z sub-frames