## Slide 1: WF on LAA DL Multi-Channel LBT with Contiguous Channels
Broadcom Corporation, CableLabs, Cisco Systems, Ruckuswireless, Orange
3GPP TSG RAN WG1 #83 R1-157629
Anaheim, USA
15th –22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background
LAA network using the DL multi-channel LBT without any restriction could not ensure the fair coexistence with another Wi-Fi 11ac/11n network in some conditions based on the simulation studies. Some key factors are
  The single LAA eNB with the non-restrictive multi-channel usage over the 5G spectrum can impact multiple 11ac/11n APs for the channel access.
  The LAA eNB with the non-restrictive multi-channel usage can have the asynchronous channel access between the channels with the wide frequency separation. (That is one channel can continuously run LBT while other channel (s) is (are) transmitting.)

## Slide 3: Proposal 1
If the LAA eNB is aware of the absence of Wi-Fi 11n/11ac devices on the set of channel (s) that it intends to transmit,
  The LAA eNB can choose either Alt2 or Alt1 (pending 3GPP decision) without restriction on multi-channel selection or multi-channel transmission.
Otherwise, the proposal on the ensuing slide apply

## Slide 4: Proposal 2
If the maximum number of the unlicensed channels the LAA eNB can simultaneously transmit on is equal or less than 4
  The set of channels on which multi-channel LBT is performed by LAA eNB shall be contiguous.
  The maximum number of unlicensed channels for eNB to perform LBT on shall not exceed the max number of unlicensed channels the LAA eNB can simultaneously transmit on.
  The final multi-channel usage based on LBT outcome could be non-contiguous.

## Slide 5: Proposal 3
If the maximum number of the unlicensed channels the LAA eNB can simultaneously transmit on is larger than 4
  The set of channels on which multi-channel LBT is performed by LAA eNB cannot exceed two groups.
    Within each group, the channels shall be contiguous
  The maximum number of unlicensed channels for eNB to perform LBT on shall not exceed the max number of unlicensed channels the LAA eNB can simultaneously transmit on.