## Slide 1: WF on LAA DL Multi-Channel LBT Channel Alignment
Broadcom Corporation, CableLabs, Cisco Systems, Ruckuswireless, Orange
3GPP TSG RAN WG1 #83 R1-157630
Anaheim, USA
15th –22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background
LAA network using the DL multi-channel LBT without any restriction could not ensure the fair coexistence with another Wi-Fi 11ac/11n network in some conditions based on the simulation studies. Some key factors are
  The LAA eNB with the contiguous multi-channel usage could not avoid the cases of the partially overlapped channels with Wi-Fi network.
  LAA need coexist with Wi-Fi in the scenario where there are nodes with the mixed channel bandwidth access capabilities.
The following proposals are the continuation of “WF on LAA DL Multi-Channel LBT with Contiguous Channels”

## Slide 3: Proposal 1
Principle: LAA eNB Multi-channel transmission should avoid transmission solely on secondary channels of one or more 11ac/11n BSS.
If a LAA eNB detects presence of 11ac/11n nodes operating on the channels that the eNB intends to transmit on,
  For Alt1
    The channel on which eNB performs Cat 4 LBT should align with one primary channel of a 11ac/11n BSS (if applicable)
  For Alt 2
    The set of channels on which LBT is performed shall consist of at least one primary channel of a 11ac/11n BSS (if applicable).
    To be eligible for multi-channel transmission, if the earliest channel does not overlap with primary channel of any 11ac/11n BSS, the earliest channel shall self-defer (including sensing for idle interval) until at least the LBT procedure for the channel overlapping with a primary channel of any 11ac/11n BSS is complete.

## Slide 4: Proposal 2
If LAA eNB does not have the capabilities (e.g. through eNB detection, UE reporting) to detect the presence of co-channel Wi-Fi 11ac/11n nodes
  Adopt Alt 2 scheme
  LAA eNB multi-channel LBT need have the mandatory minimum self-defer duration X slots to compensate for the lower channel access probability for Wi-Fi 11ac/11n in the partially overlapped channel cases.
    FFS: value of X (e.g. 10)
    The set of channels on which Cat-4 LBT occurs and the set of channels on which one-shot LBT occurs shall not be changed in a dynamic manner.