## Slide 1: WF on ED Threshold Adaptation
Ericsson
3GPP TSG RAN WG1 #83 R1-157641
Anaheim, USA
15th – 22nd November, 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Solution Alt. 1
For deployment environments that are known not to have any co-existing IEEE 802.11a/n/ac networks on the same carrier OR for eNBs that are able to detect the start and duration of IEEE 802.11a/n/ac transmissions at a received energy level of -82 dBm (over a 20 MHz channel) and that can avoid transmitting during such ongoing IEEE 802.11a/n/ac transmissions OR for eNBs that do not contend for the channel more than 50% of the time,
  the maximum energy detection threshold is set to Tmax.
For other conditions, the eNB shall set its energy detection threshold T for an LBT procedure leading to the transmission of a transmission burst as
  T = min(Tmax, Tmax – 10 + (PH – PTX) ),
  where
  Tmax = -75 dBm/MHz+ 10*log10(BW), if PH ≥ 23 dBm,
  Tmax = -75 + (23 - PH) dBm/MHz+ 10*log10(BW) (MHz), if PH < 23 dBm,
  PH is the maximum allowed EIRP in the band,
  BW is the channel bandwidth in MHz,
  PTX is the maximum transmit power within the transmission burst

## Slide 3: Solution – Alt. 2
For deployment environments that are known not to have any co-existing IEEE 802.11a/n/ac networks on the same carrier OR for eNBs that are able to detect the start and duration of IEEE 802.11a/n/ac transmissions at a received energy level of -82 dBm (over a 20 MHz channel) and that can avoid transmitting during such ongoing IEEE 802.11a/n/ac transmissions OR for eNBs that have unsuccessfully attempted to access the channel for the past Z ms,
  the maximum energy detection threshold is set to Tmax.
For other conditions, if more than Z ms have elapsed since the end of the last period of Z ms where the eNB was unsuccessful in accessing the channel, the eNB shall set its energy detection threshold T for an LBT procedure leading to the transmission of a transmission burst as
  T = min(Tmax, Tmax – 10 + (PH – PTX) ),
  where
  Tmax = -75 dBm/MHz+ 10*log10(BW), if PH ≥ 23 dBm,
  Tmax = -75 + (23 - PH) dBm/MHz+ 10*log10(BW) (MHz), if PH < 23 dBm,
  PH is the maximum allowed EIRP in the band,
  BW is the channel bandwidth in MHz,
  PTX is the maximum transmit power within the transmission burst

## Slide 4: Proposal
Select Alt. 1 or Alt. 2