## Slide 1: WF on CSI processing relaxation for FD-MIMO
Qualcomm, LGE, CATT
3GPP TSG RAN WG1 Meeting #83 R1-157659
Anaheim, USA, 15th-22nd 2015
Agenda item: 6.2.4.1

## Slide 2: Background
In Rel-11, SupportedCSI-Proc was introduced to limit the UE complexity related to CSI reporting
  Allowed values: {1, 3, 4}
Relaxations to the CSI feedback processing timeline were introduced to alleviate CSI computational complexity of multiple CSI processes
In Rel-13, a CSI process can be configured with K CSI-RS resources for reporting class B
  K CSI-IM resources are also possible

## Slide 3: Proposal
Consider the following to alleviate CSI computational complexity for FD-MIMO
  CSI processing timeline relaxation, e.g., extending from 4 to 5, retained for FD-MIMO for class A and class B with K>1