## Slide 1: Way forward on SRS for eMTC
InterDigital, CATT
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda Item: 6.2.1.11
R1-157689

## Slide 2: Proposal (1)
For Mode A
  Both periodic and aperiodic SRS is supported
For Mode B
  Both aperiodic and periodic SRS are not supported

## Slide 3: Proposal (2)
For Mode A
  Reuse existing R12 SRS
  No repetition is used
  SRS is dropped if PUSCH or PUCCH needs to be retune due to the SRS transmission
  The last symbol of PUSCH is rate-matched around if it collides with cell-specific SRS (i.e., legacy behaviour)
  The shortened PUCCH is used in a cell-specific SRS subframe based on ackNackSRS-SimultaneousTransmission configuration signalled in MTC-SIB (i.e., legacy behaviour)
For Mode B
  The last symbol of PUSCH is punctured if it collides with cell-specific SRS to allow symbol level combining
  The shortened PUCCH is used in a cell-specific SRS subframe based on ackNackSRS-SimultaneousTransmission configuration signalled in MTC-SIB (i.e., legacy behaviour)