## Slide 1: WF on SIB1bis Transmission
Huawei, HiSilicon
R1-157712
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.9

## Slide 2: Background
Agreements from RAN1#83
  6 TBS values are supported for SIB1bis
  Support {4, 8, 16} SIB1bis transmissions per 80ms
  For a given number of SIB1bis transmissions, the set of subframe(s) to be used for SIB1bis are fixed or predefined in the specification, FFS details
  The duration over which the content of SIB1bis that the UE can assume to NOT change is
    Fixed in specification to N radio frames
      Working assumption: N=512, which can be further discussed especially considering possible input from RAN2
  5 bits in MIB are used to indicate information related to SIB1bis, low cost MTC support, and/or coverage enhancement support

## Slide 3: Proposal
5 MIB spare bits are used to indicate TBS and RSIB1bis via a table
Value | TBS | RSIB1bis in BW>3MHz | (RSIB1bis, sf config) in BW<=3Hz
0 | No SIB1bis transmission |  | 
1 | TBS1 | 4 | (4,0)
2 | TBS1 | 8 | (4,1)
3 | TBS1 | 16 | (4,2)
4 | TBS2 | 4 | (4,0)
5 | TBS2 | 8 | (4,1)
6 | TBS2 | 16 | (4,2)
7 | TBS3 | 4 | (4,0)
8 | TBS3 | 8 | (4,1)
9 | TBS3 | 16 | (4,2)
10 | TBS4 | 4 | (4,0)
11 | TBS4 | 8 | (4,1)
12 | TBS4 | 16 | (4,2)
13 | TBS5 | 4 | (4,0)
14 | TBS5 | 8 | (4,1)
15 | TBS5 | 16 | (4,2)
16 | TBS6 | 4 | (4,0)
17 | TBS6 | 8 | (4,1)
18 | TBS6 | 16 | (4,2)
19 - 31 | Reserved |  | 

## Slide 4: Proposal
  Time location is determined from RSIB1bis and PCID for BW > 3 MHz
RSIB1bis | Time Allocation |  |  |  | 
 | PCID | FDD |  | TDD | 
 |  | System frame number | Subframe number | System frame number | Subframe number
4 | even | even | 4 | odd | 5
 | odd | odd | 4 | odd | 0
8 | even | any | 4 | any | 5
 | odd | any | 9 | any | 0
16 | even | any | 4 and 9 | any | 0 and 5
 | odd | any | 0 and 9 | any | 0 and 5

## Slide 5: Proposal
For BW = 3 MHz, PBCH repetition is only in SF#0 in all frames for TDD
Time location is determined from RSIB1bis and PCID
  For BW <= 3 MHz, only RSIB1bis = 4 is supported
RSIB1bis Sf config | Time Allocation |  |  |  | 
 | PCID | FDD |  | TDD | 
 |  | System frame number | Subframe number | System frame number | Subframe number
0 | even | even | 4 | odd | 5
 | odd | odd | 4 | odd | 5
1 | even | even | 5 | even | 1
 | odd | odd | 5 | odd | 1
2 | even | even | 9 | even | 6
 | odd | odd | 9 | odd | 6

## Slide 6: Proposal
For BW > 3 MHz, the two middle narrowbands are not used for SIB1bis transmission
In case of collision between SIB1bis transmissions and M-PDCCH/PDSCH repetitions,
  Drop M-PDCCH/PDSCH subframe, the unavailable subframe is counted in the repetition