## Slide 1: Way forward on UCI for eMTC
NTT DOCOMO, …
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda Item: 6.2.1.8
R1-157716

## Slide 2: Proposals (CSI measurement NBs)
  No RRC signalling for CSI measurement subset restriction is introduced.
  When M-PDCCH is configured with frequency hopping, CSI measurement is performed for the NBs used for M-PDCCH monitoring
    This implies that there is no new RRC signalling involved
  When M-PDCCH is not configured with frequency hopping, no new RRC signalling is necessary for CSI measurement
    FFS the NB(s) used for CSI measurement
    NB used for M-PDCCH monitoring is used

## Slide 3: Proposals (Definition of Wideband Narrow-band CQI)
Sub-band CQI is replaced by narrow band CQI.
  i.e., a sub-band size of six is always assumed.
Wideband CQI is supported.
  Wideband CQI is obtained using all the NBs used for M-PDCCH monitoring
    Note that wideband CQI is the same as NB CQI when the M-PDCCH is not configured with frequency hopping.

## Slide 4: Proposals (Reference resource and CQI table)
M is equal to the minimum value of R in the set of repetition numbers of PDSCH provided by higher layer signaling.
  Common value of M is used between wideband and subband CSI.
64QAM entries in CQI table are replaced with lower spectral efficiency values
  Discuss the details. See an example in R1-156418

## Slide 5: Proposals (CSI feedback mode)
For mode A UE,
  Mode 3-0 (TM1, 2, and 9) and Mode 3-1 (TM6 and 9) are supported.
  Mode 1-0 (TM1, 2 and 9) and Mode 1-1 (TM6 and 9) are supported.
For mode B UE, no CSI feedback is supported.
  Only CRS-based measurement is supported.