## Slide 1: WF on physical layer aspects of PRACH transmission
Ericsson, Huawei, HiSilicon, Nokia Networks, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, NTT DoCoMo
3GPP TSG RAN WG1 Meeting #83 R1-157724
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Background
Agreement:
For a given PRACH coverage enhancement level, the corresponding M-PDCCH search space scheduling RAR for the UE to monitor is derived at least based on MTC-SIB
MTC-SIB explicitly indicates the following information for M-PDCCH scheduling RAR:
  The set of numbers of repetitions or the max number of repetition (while other numbers of repetition are implicitly derived)
    To be concluded offline which one to use
  Other information related to M-PDCCH is FFS – Wang Yi (HW)
The starting subframe(s) of the search space for the M-PDCCH scheduling RAR is explicitly indicated in MTC-SIB
  The same configuration of the starting subframe(s) also applies to the case of message 3 re-transmissions and message 4
    FFS when C-RNTI is already configured for a UE
  FFS the details of the signalling – Yunjung (LGE)

## Slide 3: Proposals on PRACH resource configuration
No need to modify the PRACH resource configuration tables in 36.211, Table 5.7.1-2 ~ 5.7.1-4 in TS36.211.
It is up to eNB implementation whether PRACH resources for LC/CE UEs overlap with legacy PRACH resources or not.
The possible preamble indices for each PRACH resource set are indicated in MTC-SIB

## Slide 4: Proposals on power ramping
Clarify that the maximum transmission power is used on the highest (i.e. the 4th) PRACH repetition level.
Finalization of specification work on PRACH power ramping is assumed to be conducted by RAN2.

## Slide 5: Proposals on numbers of repetitions for PRACH
Agree on one of the following options for the possible numbers of repetitions of PRACH:
  Option A: multiple of 2, e.g. {1,2,4,8,16,32,64,128}
  Option B: multiple of 2 & 5, e.g. {2, 5, 10, 20, 40, 60}
  Option C: multiple of N where N is the maximum number of consecutive PRACH subframes within one radio frame, e.g. if max 2 consecutive SFs are configured within one RF, {1&2, 4&5, 7&8} are PRACH subframes. The repetition number can be {2, 4, 6, etc.}.