## Slide 1: WF on Msg3/Msg4 for MTC
Ericsson, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell, Nokia Networks, NTT DoCoMo
3GPP TSG RAN WG1 Meeting #83 R1-157726
Anaheim, USA, 15 - 22 November, 2015
Agenda Item: 6.2.1.10

## Slide 2: Proposals on initial Mgs3
For each PRACH repetition level, the set of numbers of PUSCH repetitions for initial Msg3 transmission is indicated in MTC-SIB derived based on a 4 bit indicator
  The values indicated for CE mode A are used for initial Msg3 transmission corresponding to PRACH repetition levels 0 to N.
  The values indicated for CE mode B are used for initial Msg3 transmission corresponding to PRACH repetition levels N+1 to 3.
    Option A: N = 1 (fixed)
    Option B: N = {1, 2} (indicated in SIB)
The number of PUSCH repetitions for initial Msg3 transmission is indicated in UL grant in RAR.

## Slide 3: Proposals on USS configuration of Msg3/Msg4
The search space configuration for M-PDCCH of Msg3 retransmission and Msg4 is the same as for M-PDCCH of RAR.
The narrowband index of M-PDCCH for Msg3 re-transmission or Msg4 transmission is determined by one of the following options:
  Option A: indicated in UL grant in RAR
  Option B: indicated in SIB
  Option C: the same as for M-PDCCH for RAR
Agree on Option A

## Slide 4: Proposals on transmission type for Msg3/Msg4
Agree on one of the following options:
  Option A: Both distributed and localized transmission type are supported for M-PDCCH scheduling Msg3 re-transmission or Msg4 transmission for LC/CE UEs.
    In this case, the transmission type is provided by one of the following
      SIBxbis
      UL grant in RAR
  Option B: Only support distributed transmission type for M-PDCCH scheduling Msg3 re-transmission or Msg4 transmission for LC/CE UEs.

## Slide 5: Proposals on DMRS scrambling initialization for USS for Msg3/Msg4
The DMRS scrambling sequence of M-PDCCH for Msg3 re-transmission or Msg4 transmission is initialized based on one of the following,
  Option A: TC-RNTI
    In this case, The TC-RNTI is referred by one of the following manner:
      Option A1: Explicitly signaled
      Option A2: A mapping indicated in RAR or defined in the specification
  Option B: PCID
Agree on Option A
  Agree on how to determine TC-RNTI (Option A1 or A2) or agree to let RAN2 decide

## Slide 6: Proposals on resource determination for Msg3/Msg4
The repetition number(s) of Msg3 re-transmission or Msg4 transmissions are indicated in the associated DCI.
  In this case, the number of bits is [2 or 3]
The narrowband index of PUSCH for Msg3 retransmission or Msg4 transmission is indicated in the associated DCI,
  which is similar as unicast PUSCH/PDSCH in CE mode A.