## Slide 1
WF on dynamic HARQ-ACK codebook adaptation
InterDigital, …
R1-157752
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th - 22nd November 2015
Agenda item 6.2.2.1.2

## Slide 2: Background
In RAN1#82bis following was agreed:
  eNodeB can configure by RRC signaling an eCA UE to determine HARQ-ACK codebook size according to either (a) or (b) as follows:
    Solution (a):
      DAI based solution is supported for dynamic HARQ-ACK codebook:
        Counter DAI in each DL assignment of one CG are used to HARQ-ACK codebook order.
          Counter DAI is incremented in frequency-first-time-second manner for TDD PUCCH CG.
          Counter DAI is incremented in carrier index for FDD PUCCH CG
          FFS: Number of bit for counter DAI
        FFS: Total DAI in each DL assignment of one CG is to indicate the total codebook size in the current subframe for the corresponding FDD PUCCH CG, up to present subframe within a bundling window for corresponding TDD PUCCH CG .
        FFS:UL DAI in UL grant is used to indicate the total codebook size within bundling window(Keep the same function in Rel-12);UL grant with UL DAI can be triggered by eNB if it is deemed necessary to further ensure the common understand between UE and eNB on the total codebook size
        FFS: Granularity of codebook
    Solution (b):
      An eCA UE determines HARQ-ACK codebook size according to the number of configured CCs (i.e. as in Rel-12)
        Fallback to PUCCH format 1a/b is supported as in Rel-12
    No additional spec impact is needed specifically for solution (b)
    Both solution (a) and solution (b) are mandatory feature as UE capability from RAN1 recommendation point of views for UEs supporting more than 5 CCs

## Slide 3: Background
In RAN1#83 following was agreed:
  The Counter DAI consists of M bits
    FFS the value of M, e.g., {2, 3}
  The Counter DAI denotes the number of serving cells/subframes with PDSCH transmission and with PDCCH/EPDCCH indicating DL SPS release
  If spatial bundling is not configured, 2 HARQ-ACK bits are reported per serving cell regardless of transmission mode as long as there is at least one serving cell configured with a transmission mode supporting 2 TBs

## Slide 4
    The Counter DAI consists of M=2 bits
    A 1-bit Remaining DAI is included
      Remaining DAI is repeated in 3 consecutive assignments, starting from final one
Proposal

## Slide 5
Robustness
Can resolve up to:
  4 missing initial DCI’s
  6 missing final DCI’s
  12 missing consecutive middle DCI’s