## Slide 1: UL HARQ operation
Qualcomm, Ericsson, Intel, CATT, Nokia,
R1-15xxxx
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.5

## Slide 2: Proposal
PUSCH HARQ operation for LC/CE UEs is Asynchronous
    The UL grant shall include the HARQ number and RV number
    The UE expects HARQ feedback (ACK/NAK) in the first MPDCCH occasion after (or including) N+4
      If no MPDCCH is received, the UE assumes ACK (Agreed in RAN2)
      MPDCCH occasion is defined based on the starting subframe for the candidate of the highest repetition number.