## Slide 1: WF on evaluation assumption on V2P
LG Electronics, CATT, NTT DoCoMo
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 16th – 20th November 2015
Agenda item: 6.2.8.2
R1-157767

## Slide 2: Proposals
  Pedestrian UE dropping model
    Urban case only with 60km/h vehicles
    Pedestrian UE dropping using spatial Poisson process with avg. inter-pedestrian UE distance of [10]m
      Pedestrian UE is dropped in the middle of the sidewalk
  Channel model between Pedestrian UE and Vehicle UE
    Reuse the vehicle-to-vehicle pathloss, fading, and shadowing models with the following modifications:
      Pedestrian UE speed is 3 km/h for the generation of fading
      Location update is not modeled for Pedestrian UE
      Antenna height and gain of Pedestrian UE are 1.5m, 0 dBi respectively
  Power consumption should be added as an additional performance metric. FFS details of this performance metric
  FFS for traffic model of V2P and P2V
  FFS any modification to the current performance metric for V2V