## Slide 1: WF on RV Cycling Setting Z
Sierra Wireless,…
R1-155702
3GPP TSG RAN WG1 Meeting #83 R1-157501
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.5

## Slide 2: Background #4 – How to set Z
RAN1#82bis agreement:
In case of PUSCH transmission from LC UEs and UEs operating coverage enhancement
  The redundancy version (RV) is cycled every Z subframes
    For no or small repetitions, Z=1
      FFS whether or not a TB can be mapped to X>1 subframes as a bundle
        Value of X FFS
    Otherwise, Z>1
      The scrambling sequences at least for PUSCH data are the same in the same Z subframes
      Z is not explicitly configured
      FFS the value of Z
  The RV cycling follows legacy RV cycling pattern i.e. RV {0,2,3,1}
TDD Background:
TDD Proposal is to set Z in mode B when R>12 to the # of consecutive UL SF in each Configuration
Notes: Notes:

## Slide 3: Proposal
For PUSCH and PDCSH RV cycling,
  Rel 13 UE in Mode A: Z=1
  Rel 13 UE in Mode B:
    For FDD: Z=4
    For TDD PUSCH Z = 5, PDSCH Z= 10
In Mode A and Mode B, PUSCH/PDSCH scrambling sequence is different in every Z subframes for the duration of repetitions
Note: the set of Z subframes correspond to all subframes in any frame, regardless of whether the subframes are valid or not for PUSCH/PDSCH transmission
Notes: Notes Mode B alternatives:
Alt1: if R >=16 then Z = 4
- Pro: always cycle all RVs regardless of Ych
- Con: for large R, Z could be bigger and allow better eNB CFO estimations
Alt2: If R >=16 then Z=Ych
- limit value of Ych that allow all the RVs to cycle
Alt3: if R>=16 then Z= min(Ych,4)
- Pro: always cycle all RVs regardless of Ych
Con: for large R, Z could be bigger and allow better eNB CFO estimations
Alt4: for all R Z= R/4
- Pro: always cycle all RVs regardless of Ych
- Pro: For large R, Z is bigger and allows better eNB CFO estimations
- Con: large range of Z which could complicate UE design
Alt5: For all R Z = Ych
- con: limit values of Ych that allow all the RVs to cycle
Alt6: For all R, Z=4
- con: does NOT allow all the RVs to cycle when R<15