## Slide 1: WF on Remaining Details on DCI
LG Electronics,, ...
R1-157811
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.7

## Slide 2: Questions
Resource allocation
  Narrowband index + 6 bit bitmap: LG
  Joint coding of narrowband index + PRB assignment
Is there any company strongly against Case 1 in CE mode B?
In terms of repetition number in CE mode B
  2 bit repetition number for PDSCH/PUSCH
  3 bit repetition number for PDSCH/PUSCH : LG
In terms of TBS computation in CE mode B
  TBS index is indicated in DCI instead of MCS (with assumption of fixed modulation order) : LG
  Repetition number is used to compute TBS
Do you see the necessity to increase M-PDCCH repetition number bits for DCI scheduling paging
For M-PDCCH scheduling paging, M-PDCCH repetition number bits:
  Alt1: Use a fixed subset of the candidates {2, 16, 64, 256} : LG
  Alt2: increase bits to 3 bits : LG (Okay)
For M-PDCCH order,
  CE level or PRACH resource indication is supported : LG
  CE level or PRACH resource indication is not supported.
A-SRS trigger
  Only in UL grant
  Only in DL grant
  In both UL/DL grant: LG
  Depending on final DCI size on UL/DL grant: LG

## Slide 3: Proposals for Unicast DL Grant
Resource allocation
  Separate coding between narrowband index and PRB assignment is used
PRB assignment
  Bitmap is used
    6 bits in CE mode A
    0 bits in CE mode B (6 PRBs are assumed to be scheduled always)
Repetition number for PDSCH
  2 bit in CE mode A, 3 bit in CE mode B
MCS
  4 bits excluding 64 QAM and reserved bits
A-SRS
  Trigger is supported only if UL grant size is equal or larger than DL grant

## Slide 4: Proposal (DL grant)
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
UL/DL flag | 1 | 1 | 
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Case 1 is used
PRB assignment | 6 | 0 | In CE mode B, 6 PRBs are always used for PDSCH scheduling.
Repetition number | 2 | 3 | 
MCS | 4 | 4 | 
FH hopping | 1 | 0 | Agreed. FH hopping can be dynamically enabled/diasbled
RV | 2 | 0 | 
TPC for PUCCH | 2 | 0 | 
NDI | 1 | 1 | 
HARQ process number | 3 for FDD 4 for TDD | 1 | 
SRS request | 1 | 0 | 
DAI | 0 for FDD 2 for TDD 0 for HD-FDD | 0 | 
HARQ-ACK resource offset | 2 | 2 | Agreed
M-PDCCH repetition number | 2 | 2 | Agreed

## Slide 5: Proposal (UL grant)
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
UL/DL flag | 1 | 1 | This field will be present if size of DCI on DL grand and UL grant is same (including potential padding)
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Case 1 is used
PRB assignment | 5 | 3 | 
FH hopping | 1 | 0 | Agreed. FH hopping can be dynamically enabled/diasbled
Repetition number | 2 | 3 | 
MCS | 4 | 4 | 
TPC for PUSCH | 2 | 0 | 
NDI | 1 | 1 | 
CSI request | 1 | 0 | 
HARQ process number | 3 for FDD 4 for TDD | 1 | 
RV | 2 | 0 | 
SRS request | 1 | 0 | 
UL index (for TDD) | 0 for FDD 2 for TDD | 0 | 
DAI (for TDD) | 0 for FDD 2 for TDD 0 for HD-FDD | 0 | 
CS and OCC index | 0 | 0 | Not used
M-PDCCH repetition number | 2 | 2 | Agreed

## Slide 6: Proposal (Paging)
DCI contents | Scheduling Paging
S_flag | 1
Narrowband index | Ceil(log2(number of narrowbands))
MCS | 3 (truncated MCS)
Repetition number (PDSCH) | 4 (from predefined set of repetition numbers)
M-PDCCH repetition number | 2

## Slide 7: Proposal
DCI sizes for M-PDCCH order
  In CE mode A: the same size to DCI M1A
  In CE mode B: the same size to DCI M1B
  Details are FFS
For PRACH repetition/CE level, the same CE level used in last successful PRACH transmission is assumed unless a CE level is indicated dynamically
  Support dynamic indication of CE level
Starting subframe and repetition number for PRACH transmission is determined based on SIB PRACH resource configuration for the CE level
In CE mode A
  Both preamble index and mask index can be indicated dynamically via M-PDCCH order
In CE mode B
  Mask index are not dynamically indicated via M-PDCCH order
    PRACH resource index is determined based on SIB PRACH resource configuration for the CE level
  Preamble index can be dynamically indicated via M-PDCCH order
    FFS whether the size of preamble index is reduced

## Slide 8: DCI Example in CE mode A
DCI field | Field size for DL grant | Field size for M-PDCCH order | M-PDCCH order purpose
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | ceil(log2(number of narrowbands)) | Set to 1’s | Used for differentiating between DL grant and M-PDCCH order
PRB assignment | 6 | Set to ‘1’s or ‘0’s depending on resource allocation type | Used for differentiating between DL grant and M-PDCCH order
FH hopping | 1 | 0 | 
Repetition number | 2 | 6 | Preamble index
MCS | 4 |  | 
RV | 2 | 4 | MaskIndex
TPC for PUCCH | 2 |  | 
NDI | 1 | 2 | PRACH resource set indication (CE level)
HARQ process number | 3 for FDD 4 for TDD |  | 
SRS request | 1 |  | 
 |  |  | Reserved
DAI | 0 for FDD 2 for TDD 0 for HD-FDD |  | 
HARQ-ACK resource offset | 2 |  | 
M-PDCCH repetition number | 2 | 2 | M-PDCCH repetition number

## Slide 9: DCI Example in CE mode B
DCI contents | Field size for DL grant | Field size for M-PDCCH order | M-PDCCH order purpose
UL/DL flag | 1 | UL flag | UL flag
Narrowband index | ceil(log2(number of narrowbands)) | Preamble index (4 bits) | 
Repetition number | 3 |  | 
MCS | 4 | Set to ‘1’s | Field differentiator (assume that MCS ‘1111’ is not used for regular DL)
NDI | 1 |  | 
HARQ process number | 1 | Set to ‘1’s | Field differentiator (assume that MCS ‘1111’ and ARO ’11’ is not used for regular DL)
HARQ-ACK resource offset | 2 |  | 
M-PDCCH repetition number | 2 | Use for M-PDCCH repetition number | Use for M-PDCCH repetition number

## Slide 10: Proposal (UL Grant)
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | NB index of Msg3 scheduling
PRB assignment | 5 | 3 | PRB location within the configured narrowband in narrowband index field.
Repetition number | 2 | 3 | The repetition level of Msg 3 is dynamically indicated based on a set of values configured by higher layers.
MCS | 3 | 3 | Truncated MCS
Narrowband location for M-PDCCH scheduling Msg3 retransmission/Msg4 | 2 | 2 | 
TPC | 3 | 0 | TPC is supported in CE mode A
A-CSI | 1 | 0 | A-CSI is supported in CE mode A