## Slide 1: WF on Rel.13 P-CSI Reporting for Class A
Samsung, Ericsson
AI: 6.2.4.3.2
3GPP TSG-RAN WG1#83 R1-157832
Anaheim, US, 16th - 20th November 2015

## Slide 2: Proposal
Rel 13 FD-MIMO supports
  Two submodes for PUCCH mode 1-1: submode 1 and 2
  PUCCH mode 2-1
Details are described in the next slides

## Slide 3: P-CSI mode 1-1 submode 1
1 full report consists of 3 reporting instances on PUCCH format 2/2a/2b
  1st instance: RI
  2nd instance: W1 ((i11 or i'11) & i12))
  3rd instance: CQI + W2 (i2)
For P-CSI mode 1-1 submode 1, Rel.13 class A codebook with Config given by RRC is assumed
  No codebook subsampling needed
W1 feedback periodicity is H' · Npd.

## Slide 4: P-CSI mode 1-1 submode 1
For 1st reporting instance,
  MRI, NOFFSET,RI, NOFFSET,CQI and Npd can be reused from the current RRC specification.
For 2nd reporting instance,
  For 3rd reporting instance
  Mi1 is a same value as MRI.

## Slide 5: P-CSI mode 1-1 submode 2
For CDMType= CDM2,
  UE measures and reports CSI based on the 4 or 8 CSI-RS ports of the first aggregated CSI-RS resource
For CDMType = CDM4,
  This submode is not supported
Using dual-stage 4Tx and 8Tx legacy codebooks
Using legacy P-CSI mode 1-1 submode 2 and procedures

## Slide 6: P-CSI mode 2-1
P-CSI mode 2-1 is identical to the legacy 8-Tx P-CSI mode 2-1, with following exception:
  Rel.13 class A codebook with Config given by RRC is assumed
    Legacy subsampling is reused for i2 for Config 2, 3, 4
    No subsampling is used for i2 for Config 1
  For PTI = 0, 2nd instance: W1 ((i11 or i’11) & i12))