## Slide 1: WF on CQI Table for eMTC
ZTE , Sony, Nokia [MTK, Ericsson…]
R1-157845
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.8

## Slide 2: Background
The number of subframes M (>1) that CSI reference resource spans is predefined or implicitly derived from CE level.
  The value of M
Alt 1: reuse existing CQI table for 64QAM, no new CQI entries
  Measurement is based M subframes
Alt 1.1: reuse existing CQI table for 64QAM, while 6 entries corresponding to the highest SEs are reserved
  Measurement is based M subframes
Alt 2: replacing 6 entries in the existing CQI table for 64QAM
  Measurement is based M subframes

## Slide 3: Proposal for CQI table for MTC UE
For MTC UE in Mode A
  Replacing 6 entries in the existing CQI table for 64QAM

## Slide 4: Proposal (Values taken from various companies tdocs)
CQI index | modulation | code rate x 1024 | efficiency
0 | out of range |  | 
1 | QPSK | [1] | [0.0019]
2 | QPSK | [3] | [0.0056]
3 | QPSK | [6] | [0.0117]
4 | QPSK | [12] | [0.0234]
5 | QPSK | [20] | [0.0391]
6 | QPSK | [40] | [0.0781]
7 | QPSK | 78 | 0.1523
8 | QPSK | 120 | 0.2344
9 | QPSK | 193 | 0.3770
10 | QPSK | 308 | 0.6016
11 | QPSK | 449 | 0.8770
12 | QPSK | 602 | 1.1758
13 | 16QAM | 378 | 1.4766
14 | 16QAM | 490 | 1.9141
15 | 16QAM | 616 | 2.4063