## Slide 1: WF on DCI Contents
LG Electronics,, ...
R1-157867
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.7

## Slide 2: Background
For DL DCI Mode B:
  Narrowband index is included in the DCI.
  In the indicated narrowband, the possible RBs are:
    {0, 1, …, 5}
    FFS: another value - Yunjung (LGE)
      E.g., {0, 1, 2, 3} or the first full RBG in the narrowband where the RBG is per Rel-12 specification

## Slide 3: Proposal for RB assignment
For DL DCI Mode B:
  Narrowband index is included in the DCI.
  In the indicated narrowband, the possible RBs are:
    {0, 1, …, 5}
    {0, 1, 2, 3}

## Slide 4: Proposals for Unicast DL Grant
Repetition number for PDSCH
  2 bit in CE mode A, 3 bit in CE mode B
MCS/TBS bit
  CE mode A: 4 bits excluding 64 QAM and reserved bits
  CE mode B: 4 bit TBS index is indicated in DCI instead of MCS (with assumption of fixed modulation order)
A-SRS
  Trigger in both DL/UL grant

## Slide 5: Proposal (DCI M1A/M0A)
DCI contents (M1A) | Size | Size | DCI Contents (M0A)
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Narrowband index
PRB assignment | 5 | 5 | PRB assignment
Repetition number | 2 | 2 | Repetition number
MCS | 4 | 4 | MCS
FH hopping | 1 | 1 | FH hopping
HARQ process number | 3 for FDD 4 for TDD | 3 for FDD 4 for TDD | HARQ process number
RV | 2 | 2 | RV
TPC for PUCCH | 2 | 2 | TPC for PUSCH
NDI | 1 | 1 | NDI
SRS request | 1 | 1 | SRS request
DAI | 0 for FDD 2 for TDD 0 for HD-FDD | 0 for FDD 2 for TDD 0 for HD-FDD | DAI
HARQ-ACK resource offset | 2 |  | 
 |  | 0 for FDD 2 for TDD | UL index (for TDD), SRS request
 | 0 | 1 | CSI request
M-PDCCH repetition number | 2 | 2 | M-PDCCH repetition number
Total (maximum) | 30 (FDD), 33 (TDD) | 29 (FDD), 34 (TDD) | 

## Slide 6: Proposal (DCI M1B/M0B)
DCI contents (M1A) | Size | Size | DCI Contents (M0A)
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Narrowband index
PRB assignment | 1 | 3 | PRB assignment
Repetition number | 3 | 3 | Repetition number
TBS | 4 | 4 | TBS
HARQ process number | 1 | 1 | HARQ process number
NDI | 1 | 1 | NDI
HARQ-ACK resource offset | 2 |  | 
M-PDCCH repetition number | 2 | 2 | M-PDCCH repetition number
Total (maximum) | 19 | 19 | 

## Slide 7: Proposal (DCI scheduling Paging)
DCI contents | Scheduling Paging
S_flag | 1
Narrowband index | Ceil(log2(number of narrowbands))
MCS | 3 (truncated MCS)
Repetition number (PDSCH) | 4 (from predefined set of repetition numbers)
M-PDCCH repetition number | 2

## Slide 8: Proposal
DCI sizes for M-PDCCH order
  In CE mode A: the same size to DCI M1A
  In CE mode B: the same size to DCI M1B
For PRACH repetition/CE level, a CE level is indicated dynamically
Starting subframe and repetition number for PRACH transmission is determined based on SIB PRACH resource configuration for the CE level
In CE mode A
  Both preamble index and mask index can be indicated dynamically via M-PDCCH order
In CE mode B
  Mask index is not dynamically indicated via M-PDCCH order
    PRACH resource index is determined based on SIB PRACH resource configuration for the CE level
  Preamble index is dynamically indicated via M-PDCCH order
Retransmission of PRACH reaches the maximum for the configured CE level, stop retransmission

## Slide 9: Proposal (M-PDCCH order, CE mode A)
DCI contents (M1A) | Size | Size | M-PDCCH order
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Set to ‘1’s
PRB assignment | 5 | 5 | Set to ‘1’s
Repetition number | 2 | 6 | Preamble index
MCS | 4 |  | 
FH hopping | 1 | 4 | Mask Index
HARQ process number | 3 for FDD 4 for TDD |  | 
RV | 2 | 2 | CE level
TPC for PUCCH | 2 |  | Set to ‘0’s
NDI | 1 |  | 
SRS request | 1 |  | 
DAI | 0 for FDD 2 for TDD 0 for HD-FDD |  | 
HARQ-ACK resource offset | 2 |  | 
 | 0 |  | 
M-PDCCH repetition number | 2 | 2 | M-PDCCH repetition number
Total (maximum) | 30 (FDD), 33 (TDD) | 29 (FDD), 34 (TDD) | 

## Slide 10: Proposal (M-PDCCH order, CE mode B)
DCI contents (M1A) | Size | Size | DCI Contents (M0A)
UL/DL flag | 1 | 1 | UL/DL flag
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | Set to ‘1’s
PRB assignment | 1 |  | Set to ‘1’s
TBS | 4 | 4 | Set to ‘1’s
Repetition number | 3 |  | 
 |  |  | Set to ‘1’
 |  | 1 | 
 |  |  | PREMABLE index
 |  | 6 | 
HARQ process number | 1 |  | 
NDI | 1 |  | 
HARQ-ACK resource offset | 2 |  | 
M-PDCCH repetition number | 2 |  | M-PDCCH repetition number
Total (maximum) | 19 |  | 

## Slide 11: Proposal (UL Grant carried in RAR)
DCI contents | Field size for CE mode A | Field size for CE mode B | Description
Narrowband index | ceil(log2(number of narrowbands)) | ceil(log2(number of narrowbands)) | NB index of Msg3 scheduling
PRB assignment | 5 | 3 | PRB location within the configured narrowband in narrowband index field.
Repetition number | 2 | 3 | The repetition level of Msg 3 is dynamically indicated based on a set of values configured by higher layers.
MCS | 4 | 4 | MCS/TBS
TPC | 3 | 0 | TPC is supported in CE mode A
A-CSI | 1 | 0 | A-CSI is supported in CE mode A
UL delay | 1 |  | 
FH hopping | 1 |  | 
Total | 20 | 14 | 

## Slide 12: Proposal
TM 6
  In CE mode A, TMPI and PMI confirmation fields are added to M1A
  In CE mode B, TM6 is not supported
TM9
  In CE mode A: Add 2 bits for antenna ports and scrambling identity to M1A
  In CE mode B: Add 2 bits for antenna ports and scrambling identity to M1A