## Slide 1: WF on Clarification on CE level
LG Electronics, Panasonic, Nokia,...

## Slide 2: Proposal for CE mode Determination for initial access
For determining DCI size, repetition number set, RV cycling parameters, power control, {L, R} set, for M-PDCCH/PDSCH/PUCCH/PUSCH for RAR, Msg 3, Msg 3 retx, Msg 4, and for unicast (before CE mode is explicitly configured to a UE)
    In case PRACH CE level 0 or 1 is used,
      CE mode A
    In case PRACH CE level 2 or 3 is used
      CE mode B

## Slide 3: Proposal
CE level is determined by the PRACH CE level of the last transmitted PRACH.
  Note that this is valid before and after the contention resolution message.

## Slide 4: CSS Related
CSS for RAR, and SS for Msg3 retx/Msg 4
  In the indicated narrowband, always 2+4 is assumed
    RBs used for 4 PRB set is {0, 1, 2, 3}
    RBs used for 2 PRB set is {4, 5}
CSS for paging
  Localized transmission is assumed
For CSS for RAR, and SS for Msg3 retx/Msg 4
  Distributed transmission scheme is assumed