## Slide 1: WF on Ych for common messages
Sony, CATT, Nokia
R1-157871
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.4

## Slide 2: Background on Ych
Agreement:
  X = Ych
    Note that there is no higher layer signalling for X
    The number of bits for configuring Ych is 2, and the possible values are CE mode dependent
    Note: Ych is applicable to the case when hopping is enabled and the case when hopping is disabled
  The values of Ych:
    CE mode A:
      FDD: Ych = {1, 2, 4, 8}
      TDD: Ych = {1, 5, 10, 20}
    CE mode B:
      FDD: Ych = {2, 4, 8, 16}
      TDD: Ych = {[1],5, 10, 20}
    FFS which set of Ych is used for paging, PRACH, RAR, Msg3, or Msg4
      Note: no new Ych set for this FFS

## Slide 3: Proposal on Ych for common messages
For PRACH, RAR, Msg3, Msg4
  RACH CE levels 0,1 use Ych for CE mode A
  RACH CE levels 2,3 use Ych for CE mode B
For paging
  use Ych for CE mode A

## Slide 4: Proposal on [1] issues for Ych for TDD
  TDD: For CE Mode B: replace [1] by 40