## Slide 1: WF on FFS points Regarding DCI contents
LG Electronics,, ...
R1-157895
3GPP TSG RAN WG1 #83
Anaheim, USA, 15th – 22nd November, 2015
Agenda item 6.2.1.7

## Slide 2: MCS Table – CE Mode A (starting point)
MCS Index | Modulation Order | TBS Index
0 | 2 | 0
1 | 2 | 1
2 | 2 | 2
3 | 2 | 3
4 | 2 | 4
5 | 2 | 5
6 | 2 | 6
7 | 2 | 7
8 | 2 | 8
9 | 2 | 9
10 | 4 | 9
11 | 4 | 10
12 | 4 | 11
13 | 4 | 12
14 | 4 | 13
15 | 4 | 14
PDSCH
MCS Index | Modulation Order | TBS Index
0 | 2 | 0
1 | 2 | 1
2 | 2 | 2
3 | 2 | 3
4 | 2 | 4
5 | 2 | 5
6 | 2 | 6
7 | 2 | 7
8 | 2 | 8
9 | 2 | 9
10 | 2 | 10
11 | 4 | 10
12 | 4 | 11
13 | 4 | 12
14 | 4 | 13
15 | 4 | 14
PUSCH

## Slide 3: TBS Table – CE mode B (staring point)
 | RB |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6
0 | 16 | 32 | 56 | 88 | 120 | 152
1 | 24 | 56 | 88 | 144 | 176 | 208
2 | 32 | 72 | 144 | 176 | 208 | 256
3 | 40 | 104 | 176 | 208 | 256 | 328
4 | 56 | 120 | 208 | 256 | 328 | 408
5 | 72 | 144 | 224 | 328 | 424 | 504
6 | 328 | 176 | 256 | 392 | 504 | 600
7 | 104 | 224 | 328 | 472 | 584 | 712
8 | 120 | 256 | 392 | 536 | 680 | 808
9 | 136 | 296 | 456 | 616 | 776 | 936
10 | 144 | 328 | 504 | 680 | 872 | 

## Slide 4: Proposal
DCI size of M-PDCCH scheduling paging or indicating SI update is
  DCI M1B
The contents of M-PDCCH scheduling paging is
  S_flag : 1 bit
  Narrowband index: ceil (log (number of narrowbands))
  PRB assignment: 1 bit
  MCS/TBS: 4 bits
  M-PDCCH repetition number: 3 bits
When S_flag is false, the followings are indicated, and the remaining bits are zero-padded
  SI_Update: 1 bit
  ETWS indication: 1 bit
  CMAS indication: 1 bit
  EAB: 1 bit
  systemModification-eDRX: 1 bit

## Slide 5: Proposal (DCI scheduling Paging)
DCI contents | Scheduling Paging | Indicating SI_Update & Others
S_Flag | 1 (True) | 1 (False)
Narrowband index + S_Flag | ceil(log2(number of narrowbands)) | Set to ‘1’s
PRB assignment | 1 | Set to ‘1’s
MCS | 4 | Used for 4 bits indication SI Update ETWS CMAS EAB
Repetition number (PDSCH) | 4 (from predefined set of repetition numbers) | (1 bt) systemModification-eDRX
 |  | (3 bits) Set to ‘0’s
M-PDCCH repetition number | 2 | 2
Total number | Same as M1B | Same as M1B