## Slide 1: WF on LAA DL Multi-Channel LBT
Broadcom Corporation
3GPP TSG RAN WG1 #83 R1-157897
Anaheim, USA
15th –22th November 2015
Agenda item: 6.2.3.1
Document for decision

## Slide 2: Background
For multi-Carrier LBT on a group carriers
  Alt1: eNB performs Cat-4 based LBT on only one unlicensed carrier
    When the eNB completes LBT on a carrier, the eNB can sense other configured carriers for a period, e.g., PIFS (25 microseconds), immediately before the completion of LBT on the carrier.
    The eNB is allowed to transmit DL data burst(s) on the carriers sensed idle according to above procedure.
    FFS: How fast the eNB can change the carrier requiring Cat-4 based LBT
    FFS: Whether to apply the Wi-Fi channel bonding rule
    FFS: Energy detection threshold used on channels not performing Cat-4 based LBT
  Alt2: eNB performs Cat-4 based LBT on more than one unlicensed carriers
    The eNB is allowed to transmit DL data burst(s) on the carriers that has completed Cat-4 based LBT with potential self-deferral (including idle sensing for a single interval) to align transmission over multiple carriers.
    FFS: If the eNB can receive on a carrier while transmitting on another carrier, freeze backoff counter(s) for the carrier(s) not transmitting while other carrier(s) is transmitting if the carriers are within X MHz apart
      FFS: X MHz
  FFS: Whether LAA supports Alt1 + Alt2 or Alt2 only.

## Slide 3: Proposal 2
For multi-Carrier LBT on a group carriers
  Alt1: eNB performs Cat-4 based LBT on only one unlicensed carrier
    The eNB can change the carrier requiring Cat-4 based LBT at the interval no less than 20ms
    No channel bonding rule
    The energy detection threshold used on channels not performing Cat-4 based LBT is same as the one used on channel performing Cat-4 LBT
    A single backoff counter should be used for all carriers on which Cat-4 LBT is performed. eNB can use the following Option 1 or Option 2:
      Option 1: One CW size is updated based on HARQ feedback for all the carriers.
      Option 2: CW size is updated independently per carrier. The maximum CW size is used to draw the backoff counter.
  Alt2: eNB performs CW window update independently for Cat-4 based LBT on more than one unlicensed carriers
    eNB can use independent backoff counters or can use a common backoff counter for multiple carriers.
      When a common backoff counter is used, the common random number shall be drawn based on the largest CW size of the carriers which were used in prior transmission
    If a common random counter is used, then after transmission of DL data burst(s) over one or multiple carriers, reset the extended CCA counter(s) for all channel(s) on which LBT was performed
    If independent random counters are used, after the transmission of DL data burst(s) over one or multiple carriers, reset the extended CCA counter(s) for all the activated LAA Scell(s) for the UE(s) which were scheduled in the burst.
  LAA supports both Alt1 and Alt2.

## Slide 4: Background
Evaluation scenario
  4 APs
    20MHz, on channels [0,1,2,3]
  4 LAA eNBs
    Transmit on 20MHz
    Do LBT on 4 channels [0,1,2,3], Use first available channel to Tx
    Resetting:
      Scheme 1: Reset the first available channel only
      Scheme 2: Reset the all 4 channels
  Step 1 (Wi-Fi with Wi-Fi), Step 2 (Wi-Fi with LAA)

## Slide 5: Background

## Slide 6: Background