## Slide 1: WF on RRC Parameters Related to PUCCH for MTC
Ericsson, Qualcomm, Sequans, ALU, ASB, NEC, ZTE, Panasonic, Nokia Networks, SONY
R1-157475
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda item 6.2.1.6

## Slide 2: Proposal: PUCCH resource determination
Implicit resource derivation for PUCCH format 1a is based on associated M-PDCCH for both CE mode A and mode B.
PUCCH resource determination is according to one of the following two alternatives:
  Alternative 1: RRC indicates a narrowband; RRC further indicates a starting offset which is defined within the narrowband; The narrowband can be differentiated per CE level
    Supported by: Sony
  Alternative 2: RRC indicates a starting offset which is defined within the whole system bandwidth; narrowband of PUCCH is implicitly determined from the starting offset; One starting offset can be defined for each CE level (or per narrowband)
    Supported by: Ericsson, Panasonic, LG, CATT, QualComm, ALU, ASB, Sequans, MediaTek, NEC,ZTE

## Slide 3: Proposal: ARO
ARO for large CE is according to one of the following two alternatives:
  Alternative 1: ARO, the same as that of EPDCCH, is defined for CE mode B.
    Supported by: Ericsson, Panasonic, LG, CATT, ALU, ASB, DOCOMO, SONY, QualComm, Nokia Networks, Sequans, NEC
  Alternative 2: No ARO
    Supported by: MediaTek, ZTE

## Slide 4: Proposal: RRC Parameter “PUCCH resource for Msg4 feedback”
PUCCH resource for Msg4 uses same handling as PUCCH resource determination associated with regular PDSCH.
Decide among three alternatives:
  Alternative 1: a dedicated field in RAR;
    Supported by: MediaTek ( Needed only in case of full/partial PUCCH collision)
  Alternative 2: a new, explicit RRC parameter in SIB for Msg4;
    Supported by:
  Alternative 3: Implicit derivation without introducing new parameter/field dedicated to Msg4 feedback;
    Supported by: Ericsson, Panasonic , LG, CATT, ALU, ASB , DOCOMO, Samsung , SONY, QualComm, Nokia Networks, Sequans,ZTE
  Note: A company can indicate support to two alternatives if they are applicable to different PRACH repetition levels, respectively

## Slide 5: Proposals on non-RRC PUCCH aspects for MTC
Ericsson, Panasonic, LG, CATT, ALU, ASB, DOCOMO, Samsung, Qualcomm, Nokia Networks, Sequans, MediaTek, NEC, ZTE, SONY

## Slide 6: Proposal: PUCCH formats
PUCCH format 1b/2b/3 are not supported by Rel-13 LC/CE UE for FDD.
PUCCH format 2b/3 are not supported by Rel-13 LC/CE UE for TDD.
For CE mode A, LC/CE UE supports PUCCH format 1/1a/2/2a only; additionally LC/CE UE supports PUCCH format 1b for TDD
For CE mode B, LC/CE UE supports PUCCH format 1/1a only.

## Slide 7: Proposal: ACK/NACK bundling
Working Assumption: ACK/NACK bundling/multiplexing is not supported for FDD
  Pending discussion on how to achieve peak data rate for PDSCH
ACK/NACK bundling/multiplexing is supported for TDD only when Rmax=1 for PDSCH
  When Rmax>1 for PDSCH, ACK/NACK bundling/multiplexing is not supported for TDD;

## Slide 8: Proposal: SR repetitions
SR repetition is transmitted in continuous UL valid subframes from the starting subframe