## Slide 1: WF for UE categories and capabilities
MediaTek, InterDigital, Intel, CATT, …
3GPP TSG RAN WG1 Meeting #83
Anaheim, USA, 15th - 22th November 2015
Agenda Item: 6.2.1.1
R1-157511

## Slide 2: Proposals for UE behavior and capability in HD-FDD
Proposal 1: For HD-FDD, type B operation is assumed.
Proposal 2: For HD-FDD, Similar to legacy behaviour, UE is expected to monitor DL transmission (e.g., M-PDCCH monitoring) unless explicitly signalled to perform UL transmission. When the UE is requested to perform UL transmission, the UL transmission is prioritized over DL reception.

## Slide 3: Proposal for UE capability
Proposal 1: CE mode A is mandatory for Rel13 LC UEs and CE mode B is optional for Rel13 LC/CE UEs.
  FFS in RAN2, e.g., RACH access for UE only supporting CE Mode A

## Slide 4: Proposals for UE category (1/2)
Proposal 1: UE DL category for eMTC is characterized as reception of the maximum 1000bits size for any transport block without simultaneous reception and only 1.4MHz bandwidth support.
Proposal 2: UE UL category for eMTC is characterized as the maximum 1000bits size only 1.4MHz bandwidth support.
Proposal 3: The total L2 buffer size is assumed to be 20000 bytes, up to be RAN2 confirmation.

## Slide 5: Proposals for UE category (2/2)
Proposal 4: Define a new UE DL category (e.g., DL Category M1)
Proposal 5: Define a new UE UL category (e.g., UL Category M1).
Proposal 6: Define a new combination of DL category M1 and UL category M1 for indication of total L2 buffer size.
Proposal 6: No indication of UE category for a combination of DL category M1 and UL category M1.